## Slide 1
5S Workplace Organisation
Training Guide | PE-05b | Process Excellence
Sort | Set in Order | Shine | Standardise | Sustain
A place for everything, everything in its place, and a problem visible the moment it appears.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
What is 5S?
Five Japanese words, one idea: an organised workplace where problems cannot hide.
PE-05b | 2
 | Original | Translation | Objective
1S | Seiri | Sort | Clearly separate necessary things and eliminate the unnecessary ones
2S | Seiton | Set in Order | Neatly arrange and identify things for ease of use
3S | Seiso | Shine | Maintain order and cleanliness; clean to inspect
4S | Seiketsu | Standardise | Constantly maintain and reinforce the first three; make it the way of working
5S | Shitsuke | Sustain | Always conform to the rules; build the discipline and habit
5S is not a clean-up campaign. It is the foundation discipline of lean: problems cannot be clearly seen when the workplace is disorganised, and making problems visible is the first step of improvement.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
Why 5S works
The payback is measured in safety, quality, time and morale.
PE-05b | 3
Safety
Clear walkways, no trip hazards, no leaks underfoot, nothing stored overhead that should not be. Most sites see near misses fall first.
Quality
Right tool, right material, right revision, every time. Segregated stock and labelled locations remove whole families of mix-up defects.
Time
No searching. A minute lost hunting for a tool, gauge or document, many times a day, across every person, is an enormous hidden cost.
Visibility
Abnormality stands out instantly: a missing tool, an overflowing bin, a leak. The workplace itself tells you when something is wrong.
Morale
People take pride in an area they organised themselves. Ownership of the workplace is the seed of ownership of improvement.
Credibility
Customers and assessors read your shop floor in the first five minutes of a visit. An organised site signals a controlled process.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3

## Slide 4
What F4N verification looks for
A sustainable 5S process driving improvement as part of a CI strategy.
PE-05b | 4
1
Introduced properly
Evidence of how 5S was launched: implementation plan (PE-05e), trained teams, baseline photos, red tag events. A one-off blitz with no plan behind it scores poorly.
2
Sustained by audit
A live audit system: who audits, how often, scored against what standard, and what happens to the findings. PE-05a is built to be that evidence.
3
Visible on the floor
The assessor will see it on the site tour: floor markings, shadow boards, labelled locations, area boards with scores and trends (PE-05d).
4
Owned by the teams
Employees engaged in their own areas: they can explain the standards, they raise the actions, and improvement examples trace back to 5S activity.
The question the assessor is really asking: is this a way of working, or was it tidied for my visit?
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4

## Slide 5
5S in a nuclear supply chain
In nuclear work, workplace organisation is a quality and safety control, not housekeeping.
PE-05b | 5
Material segregation
Nuclear-grade and commercial-grade material, certified and uncertified stock, conforming and quarantined parts: 5S locations and labelling make segregation physical, not procedural.
Foreign object prevention
Loose fasteners, swarf, broken tooling and stray consumables are foreign object hazards in nuclear components. Shine routines and shadow boards are your FOD controls.
Traceability protection
Controlled documents, route cards and certificates each get a designated home. A drawing of the wrong revision left at a workstation is a nonconformance waiting to happen.
CFSI defence
Counterfeit and suspect items thrive in cluttered stores. A sorted, labelled, quarantine-disciplined goods area is one of your strongest practical CFSI barriers.
See the Nuclear Awareness category of the toolkit for full guidance on safety culture and CFSI.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 5

## Slide 6
Before you start
An hour of preparation saves a wasted launch.
PE-05b | 6
1
Pick a pilot area
Choose one area with a willing team and visible pain: a workshop bay, the stores pick face, a maintenance cage. Success here sells 5S to everyone else.
2
Take baseline photos
Photograph the area exactly as it is, from fixed points you can repeat. Before-and-after photos are your most persuasive evidence, internally and at verification.
3
Form the area team
The people who work in the area do the 5S, with a facilitator. 5S done to a team by outsiders does not survive the first week.
4
Set up the basics
Red tags and a holding area (PE-05c), the audit sheet (PE-05a), camera, labels, floor tape, cleaning kit. Book the time: a focused day for the first three Ss.
The implementation roadmap (PE-05e) lays this out phase by phase for a full site roll-out.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 6

## Slide 7
1S Sort: only what is needed
If in doubt, move it out.
PE-05b | 7
Separate what the work actually needs from everything else. The test is use, not value: an expensive jig that has not been used in two years does not earn its place at the workstation. Decide by frequency of use:
Frequency of use | Where it lives
Hourly or daily | At the point of use, within reach
Weekly or monthly | In the area, but off the workstation
Rarely (under once a year) | Central store, away from the workplace
Never / unknown | Red tag it: disposition decision required
What to look for
Tools and gauges nobody has used in months
Obsolete fixtures, patterns and tooling
Out-of-date drawings, documents and labels
Excess WIP and over-ordered consumables
Broken equipment awaiting a repair that never comes
Personal accumulations: keep these reasonable and designated, and never red tag people's family photos or plants without conversation
Output of Sort: a visibly emptier workplace, a full red tag holding area, and a disposition list with dates.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 7

## Slide 8
The red tag process
A fair, visible way to challenge every item's right to be there.
PE-05b | 8
Tag
Anything not clearly needed gets a red tag (PE-05c): what it is, where found, why tagged, by whom. One tag per item; tag fairly across all areas; never tag people or reasonable personal items.
Move
Tagged items go to a designated red tag holding area, out of the workplace but visible. Remove obvious rubbish immediately; it needs a bin, not a tag.
Decide
Within an agreed period (one to two weeks works well), a named decision-maker dispositions every tag: return, relocate, store centrally, sell, scrap.
Record
Log the outcome on the tag and the disposition list. Space freed, items scrapped and value recovered make a powerful first improvement story.
Rules that keep it honest: if in doubt, move it out; do not compromise; one decision date for every tag, and no tag quietly returning to the workplace without a decision.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 8

## Slide 9
2S Set in Order: a place for everything
Make the workplace self-explanatory: anyone can find anything, and a missing item is obvious.
PE-05b | 9
Locate by frequency
The most-used items closest to the hands that use them. Heavy items at waist height; rarely used items further away.
Shadow boards
Tool outlines or foam cut-outs: one glance shows what is present, what is missing, and where everything returns.
Floor marking
Tape or paint walkways, equipment footprints, bin positions, pallet and trolley parking, quarantine and red tag zones.
Labels and addresses
Every rack, shelf, bin and drawer gets an address; every item gets a labelled home. Min/max marks on consumables make reordering visual.
Point-of-use storage
Kits, fixtures and documents staged where the work happens, in the quantity the work needs: no more, no less.
Make return easy
If putting something back takes longer than dumping it, it will be dumped. Design locations for the lazy moment, not the ideal one.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 9

## Slide 10
3S Shine: clean to inspect
Cleaning is inspection in disguise. The cloth finds the leak before the breakdown does.
PE-05b | 10
Shine restores the area to its proper condition and keeps it there: floors free of debris, machines free of grease build-up, no loose wires, no leaks left unexplained. The deeper purpose is inspection. The person cleaning a machine is the first to feel the loose guard, see the weeping seal, smell the overheating motor. Every abnormality found during cleaning is raised, tagged or logged, never just wiped away. Link Shine to your planned maintenance programme (PE-07): cleaning standards and operator care routines are the first layer of TPM.
Make Shine stick
Define what clean means per zone, with a photo of the standard
Assign every zone to a named person or small team
Set the routine: five to ten minutes at shift end beats an hour on Friday
Keep cleaning kit designated, stocked and in its own 5S order
Treat recurring contamination as a problem to solve at source (PE-04), not a fact of life to keep wiping
Goal: cleaning effort falls over time because the sources of dirt are eliminated, not because anyone stopped caring.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 10

## Slide 11
4S Standardise: make it the way of working
The method that keeps Sort, Set in Order and Shine from unravelling.
PE-05b | 11
1
Photo standards
A photograph of the area in its correct condition, posted in the area. The standard is visual: compare reality to the photo in seconds.
2
Checklists and routines
Daily and weekly 5S routines built into the working day, with tick-off visible on the area board. What gets checked gets kept.
3
One site language
Common colours, label formats, floor marking codes and min/max conventions everywhere, so anyone can read any area instantly.
4
Questions that test it
Does everything have a specific place? Is it easy to use? Easy to return? Are cleanliness standards defined? Does the layout help or fight the standard?
When an audit finds the same abnormality twice, the standard is the suspect: root cause it (PE-04) and fix the standard (PE-06), not just the symptom.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 11

## Slide 12
5S Sustain: keep it alive
Discipline beats enthusiasm. Build the habit into the rhythm of the site.
PE-05b | 12
1
Audit rhythm
Scored audits (PE-05a) weekly during roll-out, monthly once embedded. Rotate auditors; nobody audits their own area. Publish every score.
2
Leadership walks
Leaders walk the areas regularly, review the boards, ask the team about their standards, and thank people by name. Attention from the top sustains attention everywhere.
3
Visible ownership
The Area Responsibility Board (PE-05d) names the team, the zones, the routines and the latest score. Anonymous areas decay; owned areas improve.
4
Recognition and competition
Celebrate best area, most improved, best before-and-after. Light competition between areas keeps energy up long after the launch excitement fades.
Tie 5S to daily management: the audit score is a natural KPI for the S and Q pillars of your SQDCP boards (PE-03).
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 12

## Slide 13
The 5S audit
Twenty-five criteria, five per S, scored 1 to 5. Maximum 125.
PE-05b | 13
PE-05a contains the full audit system: the scored audit sheet, a scoring guide that defines what each level looks like (so two auditors give the same area the same score), the action log, a 12-month trend tracker per area, and the audit schedule with auditor rotation. Audit rules that matter:
Score what you see, not what you are told
If torn between two scores, give the lower and say why
Every 1 or 2 becomes an action with an owner and a date
Audit the audit: are actions closing? Are scores honest?
Score bands (out of 125)
105 to 125
Excellent: a reference area for others
85 to 104
Good: sustain and refine the standards
60 to 84
Developing: focus on standardise and sustain
Below 60
Needs improvement: re-run sort and set in order
The score directs attention; the trend tells the truth. A falling trend is a sustain problem even if the absolute score still looks respectable.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 13

## Slide 14
Running a 5S launch day
One focused day takes a pilot area through the first three Ss.
PE-05b | 14
1
Brief
Train the area team on the five Ss and the red tag rules. Walk the area together; agree the boundaries and take the baseline photos.
2
Sort
Red tag sweep of the whole area. Everything questionable is tagged and moved to the holding area. Rubbish goes straight out.
3
Set in Order
Plan locations by frequency of use, then build: shadow boards, labels, floor marking, min/max marks. Photograph the new standard.
4
Shine
Deep clean to inspection standard. Log every abnormality found: leaks, damage, wear. Assign cleaning zones and routines.
5
Close
Compare before-and-after photos, agree the photo standards and checklist, set the first audit date, and celebrate with the team.
Standardise and Sustain start the next morning, not at the next event: the daily routine, the board and the audit calendar are what make the day permanent.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 14

## Slide 15
5S beyond the shop floor
Offices, shared drives and inboxes hide as much waste as any workshop.
PE-05b | 15
Office 5S
Apply the same five steps to desks, filing, stationery and meeting rooms: sort the paperwork, give supplies a labelled home, define the clear-desk standard, audit it like any other area.
Digital sort
Shared drives accumulate digital clutter: obsolete versions, duplicate folders, personal copies of controlled documents. Archive or delete against agreed retention rules.
Digital set in order
One agreed folder structure and naming convention; controlled documents in one place with one live revision (supports your document control and PE-10).
Digital sustain
Quarterly digital audits: orphaned files, broken links, out-of-date templates. A cluttered drive causes wrong-revision errors just as surely as a cluttered bench.
F4N's lean expectations now include digital waste; an organised information workplace is part of the same discipline.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 15

## Slide 16
Why 5S programmes fail
Every failed 5S effort fails in one of a few familiar ways. Plan against them.
PE-05b | 16
The blitz that faded
A big launch, impressive photos, then decay within months. Cause: no audit rhythm, no routines, no ownership. Fix: 4S and 5S were never actually started.
Done to, not done by
An improvement team organises someone else's area. The team feels policed, not proud, and quietly restores the old chaos. Fix: the area team leads; facilitators support.
5S as cleaning
Treating 5S as housekeeping for visitors. The deeper purposes (visibility of abnormality, error prevention, inspection through cleaning) never engage. Fix: train the why, not just the what.
Scores without actions
Audits happen, scores are filed, nothing changes. The system becomes wallpaper. Fix: every low score becomes an owned action; leadership reviews the log, not just the number.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 16

## Slide 17
Measuring the impact
5S should pay for itself visibly. Measure before and after, then keep measuring.
PE-05b | 17
Audit score trend
The headline measure per area and for the site: out of 125, tracked monthly in PE-05a.
Search time
Time five common retrieval tasks (a tool, a gauge, a document, a fixture, a consumable) before and after. The reduction is pure productivity.
Space freed
Square metres recovered by Sort: freed racking, cleared floor, emptied cupboards. Often enough to defer an expansion.
Safety signals
Near misses, slip/trip reports and workplace inspection findings (link to your H&S programme): these usually move first and fastest.
Value recovered
Scrap value, sold equipment, returned stock and avoided purchases from the red tag dispositions.
Defect families
Mix-up, wrong-revision and missing-part defects, before and after: the quality dividend of Set in Order.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 17

## Slide 18
Summary and getting started
The whole 5S toolkit: PE-05a to PE-05e. Start with one area, this month.
PE-05b | 18
Remember
5S makes problems visible; that is its real job
Sort by frequency of use; if in doubt, move it out
A place for everything, labelled, easy to return
Cleaning is inspection: raise what you find
Standards are visual: photos, checklists, one site language
Audits with actions sustain it; scores alone do not
The area team owns its area, always
Your first steps
Choose a pilot area and take baseline photos
Print red tags (PE-05c) and set up a holding area
Run a launch day: Sort, Set in Order, Shine
Put up the Area Responsibility Board (PE-05d)
Book the first audit in PE-05a and publish the score
Plan the site roll-out with the roadmap (PE-05e)
An organised workplace is not the goal. It is the platform everything else stands on.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 18