## Slide 1
PE-02e
PROCESS EXCELLENCE
Managing Value
and Waste
HOW TO UNDERSTAND
AND COMPLETE A
VALUE STREAM MAP
A practical step-by-step guide for manufacturing businesses
entering the UK nuclear supply chain
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
How to Use This Guide
What is VSM?
Why Do It?
START
PART 1
Create the Current
State Map
Gate
Checklist
1
← review if needed
PART 2
Create the Future
State Map
Gate
Checklist
2
END
PART 1: CURRENT STATE (Steps 1–8)
Step 1
Define scope & customer requirements
Step 2
Map process steps
Step 3
Capture process data
Step 4
Map inventory
Step 5
Map material flow
Step 6
Map information flow
Step 7
Add timeline & calculate efficiency
Step 8
PART 2: FUTURE STATE (Steps 9–15)
Step 9
Confirm customer requirements
Step 10
Design for continuous flow
Step 11
Define control system
Step 12
Calculate future state metrics
Step 13
Assess people requirements
Step 14
Draw the future state map
Step 15
Set targets and action plan
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
Objectives and Principles
Value Stream Mapping: What Is It?
A visual method of representing the complete end-to-end process, the big picture, not just one area
A snapshot in time of the current system, showing where value is being added and where it is not
A tool that makes the following visible:
All the steps in a process, starting from the customer end and working backwards
Physical material flow through each process step towards the customer
Information flow: what tells each step what to do and when
The connection between information and material flow
The total lead time versus the value-adding time in the process
A structured way to identify waste across the whole value stream, not just within individual departments
A blueprint for improvement that generates the improvement roadmap rather than isolated projects
"Whenever there is a product for a customer,
there is a value stream. The challenge lies in seeing it."
SUPPLIER
PROCESS A
CT: 12 min
C/O: 8 min
Uptime: 88%
INV
PROCESS B
CT: 45 min
C/O: 30 min
Uptime: 72%
C/O too high!
INV
48 units
CUSTOMER
12m VA
2d wait
—
4.8d wait
45m VA
0.4d wait
20m VA
0.5d wait
Total Lead Time: 7.7 days | VA Time: 57 mins | Process Efficiency: 0.5%
Example: a VSM reveals that 99.5% of lead time adds no value for the customer
What the customer sees
Lead time of 7.7 days. But only 57 minutes of actual work. The rest is waiting.
Where to focus
The large inventory before Process B and the 30-min changeover are the priority targets.
What a VSM enables
You can now design a future state that could reduce lead time to under 2 days.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3

## Slide 4
Objectives and Principles
Value Stream Mapping: Why Do It?
1
Creates a shared picture of how the process really works, not how it was designed to work
When a team walks the value stream together for the first time, they often discover significant differences between what the procedure says and what actually happens.
2
Makes waste visible to everyone, not just quality or engineering
Waiting, excess inventory, unnecessary movement, and rework are often invisible to people who work in them every day. The VSM forces them to the surface with data.
3
Generates a blueprint for improvement rather than isolated projects
Without a VSM, improvement efforts tend to focus on local optimisation. A process step gets faster, but the queue in front of it simply grows. The VSM shows the whole system.
4
Synchronises production with customer demand
Takt time, the rate at which the customer requires product, becomes the foundation for every decision about flow, batch size, and staffing.
5
Provides a benchmark to measure progress against
The current state map is a dated record. When you draw the future state and achieve it, you have evidence of improvement that is visible, quantified, and credible.
6
Connects lean tools to a strategic purpose
SMED, kanban, 5S, standard work, and pull scheduling all make more sense when they are placed in the context of a value stream with measured lead times and process efficiencies.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4

## Slide 5
1
PART ONE:
Create the Current State Map
Steps 1 through 8
NucCol Ltd | Process Excellence | PE-02e
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 5

## Slide 6
Before You Start
VSM Symbols: The Language of the Map
These symbols are the standard notation for VSM. Use them consistently so that anyone familiar with lean mapping can read your map immediately.
PROCESS STEPS & DATA
Process box:
Rectangle with process name above a data box. One box per operation.
Data box:
Beneath each process box. Records CT, C/O, Uptime %, Operators, Batch size.
Operator circle:
Small circle inside or below the process box. Shows number of operators.
INVENTORY & STORAGE
Inventory triangle:
Yellow triangle with "I" inside. Quantity and time shown below.
Supermarket:
Small shelving icon. Indicates a controlled inventory point with pull signal.
Buffer/safety stock:
Separate storage location between processes or before the customer.
INFORMATION FLOW
Manual info flow:
Straight arrow. Schedule, order, or instruction passed by paper or verbal.
Electronic info flow:
Arrow with "lightning bolt". ERP system, email, MES data, digital schedule.
Production kanban:
Small card. Authorises production of a set quantity.
Withdrawal kanban:
Small card. Authorises movement of material from one point to another.
MATERIAL FLOW
Push arrow:
Striped arrow. Material is pushed to the next step regardless of need.
Pull/withdrawal:
Circular arrow. Material is only moved when a downstream signal is received.
Finished goods arrow:
Large open arrow from last process to customer.
IMPROVEMENT MARKERS
Kaizen burst:
Starburst shape (approximated as spiked box). Marks a waste or improvement opportunity.
Target value:
Value written on the kaizen burst showing the improvement goal.
EXTERNAL ENTITIES
Factory/supplier icon:
Building shape in top left. Represents the supplier of raw material or bought-in parts.
Customer icon:
Building shape in top right. Represents the end customer or next process tier.
Transport arrow:
Shows mode of transport and frequency between supplier and the value stream.
Tip: Draw your map on A3 or A1 paper with pencil first. Digital versions come after, not before. The act of physically drawing it as a team generates insights that clicking around a computer screen does not.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 6

## Slide 7
1. Create a Current State Value Stream Map
Step 1: Define Customer Requirements and Calculate Takt Time
Start every VSM exercise from the customer, not the supplier. Understanding what the customer actually needs, and at what rate, is the foundation on which every other decision is built.
What to capture about your customer:
Volume: how many units per week/day do they require?
Delivery frequency: daily, weekly, call-off?
Packaging and labelling requirements
Quality grade and inspection requirements (especially important in nuclear)
Lead time expectation: what do they expect from order to delivery?
Contractual obligations: SLAs, OTIF targets, penalties
TAKT TIME: THE HEARTBEAT OF THE PROCESS
Takt time is the maximum time available per unit to meet customer demand. It is the "drum beat" of the process and every process step should be able to meet it.
Takt Time = Available Working Time per Period
Customer Requirement (units) in same period
Example: 37.5 hr week (2,250 mins) ÷ 60 units = 37.5 minutes per unit
Customer Data Box
CUSTOMER
(Nuclear OEM Example)
Weekly volume required
60 units/week
Working hours per week
37.5 hours
Working days per week
5 days
Delivery frequency
Weekly, full consignment
Takt time (calculated)
37.5 mins per unit
Lead time expectation
10 working days
Quality grade
Nuclear Grade 2 (IFS)
OTIF requirement
≥ 95%
Packaging requirement
Individual bagged, tagged, with CoC
Key issue raised
Current supplier lead time is 22 days
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 7

## Slide 8
1. Create a Current State Value Stream Map
Step 2: Map the Process Steps
Walk the process from the customer backwards to raw material, not the other way around. This keeps your perspective anchored on what the customer needs rather than what is convenient to produce.
Walk the process, do not map from memory
Your process map and your QMS procedure will not match reality. The only way to map what actually happens is to physically walk it, observe it, and talk to the people doing the work.
Map every step, including ones that add no value
Inspection steps, waiting points, rework loops, and transport legs should all appear. The temptation to omit NVA steps defeats the purpose of the exercise.
Work backwards from the customer
Starting at despatch and working back to goods-in keeps you focused on what the customer needs at each stage.
Use different colours to indicate value
Green process boxes for value-adding steps (anything that changes the fit, form, or function of the product). Red or grey for non-value-adding steps.
Post process boxes on paper first
Use a large roll of brown paper and Post-it notes. Moving boxes around is easy on paper and almost impossible once you have committed to a digital version.
Process sequence mapped on paper (example):
GOODS IN
/ STORES
Data here
CNC
TURNING
Data here
CNC
MILLING
Data here
DEBURR
& CLEAN
Data here
CMM
INSPECTION
Data here
SURFACE
TREATMENT
Data here
DESPATCH
Data here
Colour coding guide:
Value-adding step (changes fit, form, or function)
Non-value-adding step (required but adds no value for customer)
Necessary but non-direct (goods in, despatch, planning)
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 8

## Slide 9
1. Create a Current State Value Stream Map
Step 3: Capture Process Data
For every process box, collect actual observed data, not system data, not standard times, and not what the supervisor thinks it should be. The map must reflect reality.
DATA BOX: WHAT TO CAPTURE AT EACH PROCESS STEP
Cycle Time (CT)
The time to complete one unit from start to finish at this step. Time it with a stopwatch. Measure several cycles and use the mode (most common), not the average.
Changeover Time (C/O)
The time to switch from the last unit of one product to the first good unit of the next. Include all preparation, cleaning, adjustment, and trial runs.
Uptime %
Actual production time as a percentage of planned production time. Low uptime is often caused by breakdown, changeover, or waiting for materials.
Number of operators
Count of people allocated to this step during a standard shift. Include all roles: machine operator, inspector, loader.
Batch size
How many units are processed together before moving to the next step. Large batches create large queues downstream.
OK Rate / First Pass Yield
Percentage of units that pass the process without rework or rejection. If 5% of parts need rework, record 95% here.
Number of machines
Count of machines or workstations at this step. Important for calculating capacity against Takt.
Observations
Any issues, constraints, or notable characteristics observed during the walk. Record everything; edit later.
Example completed data box (CNC turning cell):
CNC TURNING Cell 1
2
Cycle Time
42 minutes
Changeover
35 minutes
Uptime
81%
OK Rate / FPY
94.2%
Batch size
10 units
No. Machines
2
Observations
Tool wear causing scrap on final pass
Issues highlighted in red: these become targets for improvement
KEY RULES FOR CAPTURING DATA
Measure cycle time yourself with a stopwatch. Do not ask the operator what it should be
Challenge data that looks too good. 100% uptime and 0% rework are almost never real
Capture variation: if times vary significantly, note the range and use the typical (mode) value
Record what you actually see happening, not what the SOP says should happen
Be transparent with the team about what you are measuring and why
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 9

## Slide 10
1. Create a Current State Value Stream Map
Steps 4 & 5: Map Inventory and Material Flow
STEP 4: INVENTORY
Count the actual inventory at every point in the value stream between each process step, at goods in, and at finished goods.
Express inventory in two ways: the quantity held, and the number of days of demand that quantity represents based on customer consumption rate.
Do not rely on the ERP system stock figures. Walk the shop floor and count physically. System figures and physical reality frequently differ.
Days of inventory = Quantity held ÷ Customer daily requirement
Example: 45 units held, customer requires 12/day = 3.75 days of inventory
STEP 5: MATERIAL FLOW, PUSH vs PULL
PUSH
A process produces output regardless of whether the downstream step is ready for it. Push creates queues, excess WIP, and hides problems. Most factories operate predominantly on push.
PULL
A process only produces when the downstream step requests it. Pull eliminates WIP build-up and synchronises production with customer demand. This is the target of the future state.
Current state (push) versus future state (pull):
CURRENT STATE: PUSH
TURNING
45
PUSH
MILLING
38
PUSH
DEBURR
22
PUSH
INSPECT
Total WIP: 105 units queued | Lead time driven by inventory, not process speed
FUTURE STATE: PULL
TURNING
5
PULL
MILLING
4
PULL
DEBURR
3
PULL
INSPECT
Total WIP: ~17 units | Lead time falls in proportion to WIP reduction
INVENTORY AND NUCLEAR SUPPLY CHAINS
Excess inventory carries additional risk in nuclear manufacturing beyond the usual WIP cost and lead time impacts. Material held beyond its certification window may lose its approved status. Components stored incorrectly can become non-conforming through contamination, mechanical damage, or exposure. First-in-first-out (FIFO) management is an expectation of nuclear customers, and excess inventory makes FIFO harder to maintain. Nuclear customers will look at WIP levels on a site tour. High WIP is a visible indicator of push scheduling and poor flow control.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 10

## Slide 11
1. Create a Current State Value Stream Map
Step 6: Map the Information Flow
The information flow is the often-overlooked half of the value stream map. It shows what tells each process step what to do next, and it is frequently where the biggest sources of waste and delay are hiding.
Manual information flow
Straight solid arrow. A schedule, work order, verbal instruction, or printed paperwork. Common in smaller businesses. Creates waste when information is ambiguous, late, or lost.
Electronic information flow
Arrow with a zigzag or lightning bolt symbol. ERP-generated job cards, email schedules, MES instructions. Faster but not immune to errors, incorrect data in a system is worse than no data.
Informal information
Dashed or curved arrow. "I asked Dave what to do next." This is the most common information flow in most factories, and the most dangerous because it is invisible, inconsistent, and non-auditable.
KEY QUESTIONS TO ASK AT EACH PROCESS STEP
How does this step know what to make next?
Where does that instruction come from?
How often is it updated?
Mapping the information flow: example:
PLANNING
FUNCTION
(ERP / MRP)
CUSTOMER
Weekly forecast + orders
GOODS IN
ERP
TURNING
ERP
MILLING
ERP
DEBURR
verbal
INSPECT
verbal
DESPATCH
verbal
COMMON FAILURE: INFORMAL INFORMATION CONTROLS KEY PROCESSES
In the example above, the deburr and inspection steps are controlled by verbal instruction from the supervisor rather than the ERP system. This means those steps have no formal priority signal. They work on whatever is physically in front of them. In a nuclear context, this creates a traceability and scheduling risk. The future state map should show all critical steps receiving a documented, controlled information signal.
INFORMATION FLOW AND DIGITAL WASTE
Since 2020, the concept of digital waste has become a formal part of VSM thinking. Map information flow carefully and ask: Is this data re-entered into more than one system? Are there reports generated that nobody reads? Is the same drawing held in three different places? Each yes is a digital waste that carries traceability and error risk in a nuclear environment.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 11

## Slide 12
1. Create a Current State Value Stream Map
Step 7: Add the Timeline and Calculate Process Efficiency
The timeline is the most revealing part of the current state map. It converts all the inventory data and process data into a single, clear comparison: how long does it actually take versus how long is spent adding value.
How to calculate the timeline:
1
Convert inventory to days
For each inventory point: days = quantity ÷ customer daily requirement. Place these wait times on the top "steps" of the timeline.
2
Add process (VA) times
For each process step: use the cycle time. These go on the bottom "steps" of the timeline.
3
Sum the total lead time
Add all the wait times together. This is the total lead time.
4
Sum the value-adding time
Add all the cycle times together. This is the value-adding time.
5
Calculate process efficiency
Process efficiency (%) = (value-adding time ÷ total lead time) × 100.
Most UK manufacturers see process efficiencies of 1–10% on their first VSM. This is not unusual. It is the baseline from which improvement begins.
Example timeline: 6-step process:
GDS IN
TURNING
MILLING
DEBURR
INSPECT
DESPATCH
2.0d
15m
4.5d
42m
3.8d
38m
2.2d
22m
5.2d
55m
1.5d
20m
WAIT / INVENTORY TIME
VALUE-ADDING TIME (Cycle Time)
TIMELINE CALCULATIONS
Total wait time
2.0 + 4.5 + 3.8 + 2.2 + 5.2 + 1.5 =
19.2 days
Total VA time
15 + 42 + 38 + 22 + 55 + 20 =
192 minutes (3.2 hours)
Total lead time
19.2 days + 3.2 hrs =
~19.6 days (22 days quoted)
Process efficiency
192 mins ÷ (22 × 450 mins) × 100 =
1.94%
Process efficiency of under 2% means that for every hour the customer waits, less than 90 seconds involves actual work on their product. This figure is not unusual. It is the starting point. When presented to leadership teams for the first time, it almost always generates immediate commitment to improvement.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 12

## Slide 13
1. Create a Current State Value Stream Map
Step 8: Identify Waste and Mark Kaizen Bursts
The final step in building the current state map is to overlay it with kaizen bursts, visual markers that identify problems, constraints, and improvement opportunities. Every burst is a candidate for a future state change and a CSIP project.
What to mark with a kaizen burst
Any step where the cycle time exceeds Takt time (you cannot meet customer demand from this step as currently configured). Large inventory points (anything more than 1 to 2 days of demand). High changeover times that are driving large batch sizes. Poor uptime (below 80% is a clear concern). Poor quality or high rework rates. Information flow gaps or informal controls. Any process step the team identifies as a known pain point.
How to prioritise which to address first
Not all kaizen bursts are equal. Rank them by: impact on lead time; impact on quality (especially important in nuclear); impact on cost; ease of implementation. Start at the pacemaker process and work upstream, or identify the highest-impact quick win.
Linking bursts to the CSIP
Every kaizen burst on the current state map should generate a CSIP project entry. The burst identifies the problem; the CSIP project defines the solution, the owner, the target, and the timeline. This is how the map becomes an improvement programme rather than a paper exercise.
Current state map with kaizen bursts marked:
TURNING
MILLING
DEBURR
INSPECT
DESPATCH
CT > Takt
Add capacity
C/O: 35m
SMED target:
15m
Bottleneck
5.2d queue
Inline insp.
5.8% scrap
8D RCA
required
CAPACITY CHECK: CYCLE TIME vs TAKT TIME (37.5 mins per unit)
Process Step
Cycle Time
Takt Time
Status
Goods In / Stores
15 mins
37.5 mins
OK
CNC Turning Cell 1
42 mins
37.5 mins
EXCEEDS TAKT
CNC Milling Cell 2
38 mins
37.5 mins
Borderline
Deburr & Clean
22 mins
37.5 mins
OK
CMM Inspection
55 mins
37.5 mins
EXCEEDS TAKT
Despatch
20 mins
37.5 mins
OK
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 13

## Slide 14
Gate Checklist 1:
Create the Current State Value Stream Map
Before progressing to the future state, confirm that every item below has been completed. Do not skip items, the quality of the future state map depends entirely on the accuracy of the current state.
✓
The scope of the map has been agreed (high-level enterprise view, or detailed product-family level)
✓
The product family or representative part to be mapped has been identified and agreed with the team
✓
All relevant VSM symbols are understood by everyone participating in the exercise
✓
Customer requirements have been confirmed: volume, takt time, lead time expectation, quality grade, and delivery frequency
✓
The complete process sequence has been physically walked and mapped, not mapped from memory or from a procedure
✓
Process data has been gathered by direct observation at each step: cycle time, changeover, uptime, operators, batch size, and first pass yield
✓
Inventory has been physically counted at every point in the value stream, including goods-in and finished goods
✓
Material flow has been mapped and characterised as push or pull at each step
✓
Information flow has been mapped: what tells each step what to do, and whether it is manual, electronic, or informal
✓
The timeline has been drawn and the process efficiency has been calculated
✓
Kaizen bursts have been marked at all identifiable waste and constraint points
✓
The cycle time versus takt time check has been completed for every process step
✓
The current state map has been reviewed with the team and agreed as an accurate representation of reality
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 14

## Slide 15
2
PART TWO:
Create the Future State Map
Steps 9 through 15
NucCol Ltd | Process Excellence | PE-02e
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 15

## Slide 16
2. Create the Future State Value Stream Map
Steps 9 & 10: Confirm Requirements and Design for Flow
STEP 9: RECONFIRM CUSTOMER REQUIREMENTS
Before designing the future state, reconfirm the customer requirement. Has the volume changed? Has the lead time expectation shifted? Has a new nuclear programme requirement been added? The future state is designed around what the customer needs today and in the next 12 to 18 months, not what was true when the current state was mapped.
STEP 10: IDENTIFY OPPORTUNITIES FOR CONTINUOUS FLOW
Can any processes be eliminated?
Does every step genuinely transform the product in a way the customer values? Inspection steps, rework loops, and approval stages are common candidates for elimination or reduction.
Can any processes be combined?
If two adjacent steps have combined cycle times below Takt, they can potentially be run by one operator in a single cell. This eliminates the inventory point between them.
Can processes be re-sequenced?
Sometimes a step creates waste only because of where it sits in the sequence. Moving inspection earlier (closer to the point of production) can eliminate queues.
Where is flow broken?
Wherever flow cannot be maintained due to batch sizes, long changeovers, or capacity mismatches, a buffer or control mechanism is needed. Mark these as control points.
Combining processes to eliminate inventory:
BEFORE: Two separate steps with inventory point between them
DEBURR
& CLEAN
5.2-day
queue
52 units
5.2 days wait
CMM
INSPECT
AFTER: Combined step, inline first-off inspection eliminates the queue
DEBURR + INLINE INSPECTION
CT: 28 min | 1 operator | First-off check at source
Result: queue eliminated | lead time -5.2 days | same staffing
TAKT TIME RE-CHECK: DOES THE FUTURE STATE MEET DEMAND?
Takt time = 37.5 minutes per unit. With SMED reducing Cell 1 changeover to 14 minutes, Cell 1 cycle time of 42 minutes can be met on two machines (21 min effective CT per unit). The new combined Deburr + Inline Inspection step takes 28 minutes, below Takt. CMM inspection moves to FAI and periodic audit only, no longer on the critical path.
NUCLEAR CONTEXT: INSPECTION IN THE FUTURE STATE
Moving to inline inspection does not eliminate the rigour of nuclear inspection. It relocates it to the most effective point. Nuclear customers want Right First Time at source, not batch re-inspection at the end of the line. Inline first-off inspection, with results documented on the job traveller, actually provides better traceability and earlier problem detection than a centralised CMM queue. Discuss this approach with your Supply Chain Consultant before implementation.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 16

## Slide 17
2. Create the Future State Value Stream Map
Steps 11 & 12: Control System and Future State Metrics
STEP 11: DEFINE THE CONTROL SYSTEM
Kanban
A physical or electronic card that authorises production of a specific quantity. When the downstream step consumes a kanban quantity, a card is returned to the upstream step authorising replenishment. Simple and effective.
FIFO lane
A controlled buffer between two steps where material is consumed in the order it arrives. When the lane is full, the upstream step stops. When the lane has space, the upstream step starts.
Supermarket pull
A small, controlled stock of finished or semi-finished items that the downstream step pulls from as needed. Replenishment of the supermarket is triggered by consumption.
STEP 12: CALCULATE FUTURE STATE METRICS
Using the same method as the current state timeline, calculate the projected lead time and process efficiency for the future state. These figures become the targets that the improvement programme is measured against.
Metric
Current State
Future State Target
Change
Total WIP
192 units
~32 units
-83%
Total lead time
22 days
7 days
-68%
Value-adding time
3.2 hours
3.1 hours
Similar
Process efficiency
1.94%
5.6%
+189%
OTIF (projected)
74%
94%+
+20pp
Future state control system, pacemaker and pull signals:
TURNING
PACEMAKER
PULL
FIFO
MILLING
PULL
FIFO
DEBURR+
INSP.
PULL
FIFO
DESPATCH
SCHEDULE
(ERP pull signal)
Only the pacemaker
receives a schedule
Schedule only the pacemaker process
All other steps respond to pull signals from the downstream step. Only the pacemaker receives a schedule from the planning system. This prevents overproduction everywhere upstream.
Set WIP limits (kanban quantities)
Each step has a maximum WIP limit. When the downstream buffer is full, the upstream step stops. This is the mechanism that makes pull work in practice.
Use FIFO between closely linked steps
Where steps are physically adjacent and use similar batch sizes, a simple FIFO lane (maximum 3 to 5 units) is more effective than a formal kanban system.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 17

## Slide 18
2. Create the Future State Value Stream Map
Steps 13 & 14: People Requirements and Drawing the Future State
STEP 13: PEOPLE AND SKILLS REQUIREMENTS
Are existing operators able to run the new process?
If two steps are being combined, does the operator who runs step A also have the skills to perform step B? In nuclear manufacturing, this question carries additional weight because competence must be documented and verified.
What training or qualification is required?
Any change in process creates a training requirement. SOPs must be updated before the change is made, and operators must be signed off against the new procedure before production begins.
What does the skills matrix show?
The future state is the right time to update the skills matrix. Map the new combined or re-sequenced steps against current operator competencies and identify any gaps.
Is the headcount right for the new flow?
Pull scheduling typically reduces the headcount needed at some steps and increases it at others. Model the future state staffing requirements against takt time and cycle times.
STEP 14: DRAW THE COMPLETE FUTURE STATE MAP
Draw all process boxes with the new cycle times and staffing levels from the future state design
Show the new information flow: electronic pull signal to the pacemaker only
Mark FIFO lanes and kanban quantities between each step
Show the reduced inventory triangles at each buffer point
Draw the timeline with the new wait times and cycle times
Mark targets on any remaining kaizen bursts (uptime improvement, further SMED, etc.)
Add the future state metrics: lead time, process efficiency, and WIP target
FUTURE STATE MAP, Precision Engineering Ltd (7-day lead time target)
GDS IN
15m
PULL
0.5d
TURNING
42m
PULL
0.8d
MILLING
38m
PULL
0.6d
DEBURR+
INSP.
28m
PULL
0.5d
DESPATCH
20m
Lead Time: 7 days | VA Time: 3.1 hrs | Process Efficiency: 5.6% | WIP: ~32 units | OTIF Target: 94%+
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 18

## Slide 19
2. Create the Future State Value Stream Map
Step 15: Develop Targets and the Action Plan
The future state map is only valuable if it generates a concrete action plan. The map tells you what needs to change; the action plan tells you how, when, and who. Without the action plan, the VSM exercise is an interesting conversation piece, not a transformation tool.
Start at the pacemaker process
Begin implementation at the pacemaker step and work upstream. The pacemaker sets the rhythm for everything else. Getting that right first stabilises the whole value stream.
Or go for the biggest bang first
Alternatively, start at the highest-impact kaizen burst, the one that delivers the most lead time reduction, cost saving, or quality improvement. Early, visible results build momentum and commitment.
Set quantifiable targets for each action
Every action on the plan must have a measurable target. Not "improve changeover time" but "reduce changeover on Cell 1 from 35 minutes to 14 minutes by 31 March."
Phase the plan realistically
Not everything can happen at once. Sequence actions logically, if pull scheduling depends on kanban design, design the kanban first. If inline inspection depends on a new gauge, procure the gauge first.
Build in review gates
Set review points, typically every 4 to 8 weeks, where progress is assessed against targets. At each gate, decide whether to proceed, adjust, or go back to a previous step.
VSM to CSIP: converting kaizen bursts into actions
Kaizen Burst
Action
Target
Owner
Date
CSIP Ref
C/O: 35 min
→ Cell 1
SMED exercise on Cell 1 turning. Video current state, classify internal/external, trial new sequence.
CT below 15 min
Ops Mgr
31 Mar
CSIP-01
5.8% scrap
→ Cell 1
8D root cause analysis. Introduce mandatory tool life record on job traveller.
Scrap <2%
Quality Mgr
28 Feb
CSIP-02
5.2-day queue
→ Inspect
Design inline first-off inspection protocol at Cell 2. Source surface plate and go/no-go gauges.
Same-day
inspection
Quality Mgr
15 Feb
CSIP-03
Motion waste
→ Deburr
Relocate deburr station to Cell 2 area. Agree layout with facilities. Move equipment over a weekend.
Layout live
Facilities
28 Jan
CSIP-04
Push scheduling
→ All cells
Design pull system with FIFO lanes. Set WIP limits. Brief all operators. Run 2-week trial.
WIP <40 units
Ops Mgr
30 Apr
CSIP-05
Skills waste
→ All cells
Launch weekly 15-min team reviews at each cell. Train operators in 5 Whys. Log all issues raised.
Ongoing
HR / Ops
1 Feb
CSIP-06
Each row above becomes a CSIP project. The VSM exercise has generated a fully sequenced, owned, and targeted improvement programme in a single workshop.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 19

## Slide 20
Gate Checklist 2:
Create the Future State Value Stream Map
Confirm that every item below has been completed before progressing to implementation. The quality of the improvement programme that follows depends entirely on the rigour of this checklist.
✓
Customer requirements have been reconfirmed for the future state (volume, takt time, lead time, quality grade)
✓
Opportunities for process elimination, combination, or re-sequencing have been identified and evaluated
✓
The future state flow design has been agreed by the team, a clear concept exists for how material will move
✓
The control system has been designed: pacemaker identified, FIFO lanes or kanban quantities defined for each step
✓
Replenishment signals have been designed: what triggers each step to produce, and in what quantity
✓
Future state lead time and process efficiency have been calculated and documented
✓
People requirements have been assessed: skills gaps identified, training needs confirmed, staffing model reviewed
✓
The complete future state map has been drawn with all data, information flow, and control mechanisms shown
✓
Targets have been set for each kaizen burst remaining in the future state
✓
A phased action plan has been developed: actions, targets, owners, dates, and CSIP project references
✓
Review gates have been agreed: dates and criteria for assessing whether each phase has been achieved
✓
The plan has been presented to and approved by senior leadership, resource and budget are committed
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 20

## Slide 21
Reference
Takt Time: Quick Reference and Common Mistakes
THE TAKT TIME FORMULA
Takt Time = Available Working Time per Period ÷ Customer Requirement (units) in same period
Result: the maximum time allowed to complete one unit if you are to meet customer demand
WORKED EXAMPLES
Shift Pattern
Customer Demand
Available Time
Takt Time
What This Means
Single shift
(7.5 hr day)
60 units/day
7.5 hrs × 60 mins = 450 mins
450 ÷ 60 = 7.5 mins per unit
Must complete one unit every 7.5 minutes
Two shifts
(15 hr day)
120 units/day
15 hrs × 60 mins = 900 mins
900 ÷ 120 = 7.5 mins per unit
Same takt despite double the volume, both shifts needed
37.5 hr week
60 units/week
37.5 hrs × 60 mins = 2,250 mins
2,250 ÷ 60 = 37.5 mins per unit
One housing every 37.5 minutes across the working week
4-day week
(30 hr available)
5 units/day
30 hrs × 60 mins = 1,800 mins
1,800 ÷ 5 = 360 mins per unit
Low-volume, long-cycle product, 6 hours per unit
COMMON MISTAKES WITH TAKT TIME
Using gross hours instead of available time
Planned breaks, shift handovers, and planned maintenance must be deducted. If a 7.5-hour shift has 30 minutes of breaks, available time is 7.0 hours.
Using average demand instead of peak demand
If customer demand fluctuates significantly, design the future state around the typical peak, not the average. Average takt will lead to failure during high-demand periods.
Confusing takt with cycle time
Takt time is a customer requirement. Cycle time is what the process actually achieves. The goal is to get cycle time close to (but below) takt time, not to make them equal.
Not re-calculating when demand changes
Takt time is not fixed. When volume changes, takt changes. Many organisations set a takt time once and never revisit it, then wonder why their flow system breaks down.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 21

## Slide 22
Reference
Digital Waste: The 2025 Addition to Value Stream Mapping
The original seven wastes (TIMWOOD) were defined in a pre-digital manufacturing world. Since 2020, digital waste has emerged as a formal additional category, and one that is increasingly relevant to UK manufacturers seeking entry to the nuclear supply chain.
What is digital waste?
Duplicate data entry
The same information is entered into two or more systems, a paper traveller, an ERP system, and a quality database. Each re-entry is a waste of time and a new opportunity for error.
Nuclear context:
Every re-entry of data in a nuclear environment creates a new opportunity for transcription error on a quality record.
Parallel systems
The production schedule is managed in Excel, the quality system is separate, and the job card is on paper. None of them agree.
Nuclear context:
Nuclear traceability requires a single source of truth. Three parallel systems create three versions of every record.
Unreceived information
Daily automated reports that nobody reads. Meeting minutes sent to distribution lists that were never updated.
Nuclear context:
Information that is never acted upon is not information. It is noise. In nuclear, unread records can conceal NCRs.
Information delays
A design change sits in an approvals queue for a week. Production continues on the old drawing.
Nuclear context:
In nuclear manufacturing, any work on a superseded drawing is a non-conformance. Information delay is a quality risk.
Inaccessible records
Quality records stored on a retired server. Certificates filed in a folder nobody can find.
Nuclear context:
Nuclear customers require records to be retrievable for the life of the plant, 40 to 60 years in some cases.
Digital overprocessing
Using a full MRP system to schedule a 10-person workshop when a whiteboard kanban would work better.
Nuclear context:
Over-complexity in information systems creates training overhead, system dependency, and cascading failure risk.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 22

## Slide 23
Reference
VSM and the Nuclear Supply Chain: What Assessors Expect
The F4N Managing Value and Waste assessment question is asking a specific question: does this organisation have a structured, evidence-based approach to identifying and eliminating waste? A completed VSM exercise, with documentation, is the clearest possible answer.
What assessors look for
A current state map that shows the process as it actually operates, not an idealised version. Evidence that the team walked the process and gathered real data. Kaizen bursts that correspond to real, identified problems. A future state map that is realistic and achievable. An action plan where every item has an owner, a target, and a date. CSIP project entries that trace back to the VSM exercise.
What impresses a nuclear customer
A VSM exercise conducted as a team, including shop floor operators, not just management. Quantified waste: not just "we found some waiting" but "the inspection queue creates 5.2 days of lead time at a cost of £4,200 per month in missed OTIF penalties." A before-and-after comparison showing measurable improvement. Evidence that the VSM is repeated, that it is a regular management tool, not a one-off exercise.
What disqualifies an application
A VSM that was clearly drawn at a desk rather than walked. Process efficiency figures that are unrealistically high, if a company claims 30% process efficiency with no prior lean history, the assessor will investigate. Kaizen bursts with no corresponding actions. Action plans with items marked "complete" that show no measurable outcome. Maps that are months old with no evidence of any follow-up activity.
REMEMBER: EVIDENCE MATTERS MORE THAN PERFECTION
A company that can show a current state map with 2% process efficiency, a future state map with a 6% target, and a CSIP with five active improvement projects will score better in a nuclear assessment than a company that claims to have already eliminated all waste but cannot produce any evidence. Structured honesty, backed by data and action, is exactly what nuclear customers are looking for.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 23