## Slide 1
Planned Maintenance &
TPM Implementation Guide
A step-by-step guide to Total Productive Maintenance, OEE and Autonomous Maintenance for the nuclear supply chain
F4N Process Excellence Toolkit | Reference: PE-04e
PE-04e | 1
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
What is Total Productive Maintenance (TPM)?
Total Productive Maintenance (TPM) is a structured approach to maintaining and improving the integrity of production equipment through the involvement of everyone who operates, maintains, supports and manages it.
The shift in attitude
Old Attitude
“I operate, you fix.”
“I fix, you design.”
“I design, you operate.”
TPM Attitude
“We are all responsible
for our equipment.”
Why it matters in the nuclear supply chain
Unplanned equipment failure can directly affect product quality, on-time delivery and the ability to demonstrate a controlled, capable process: all core expectations of the F4N Planned Maintenance / Machine Availability assessment.
TPM delivers:
Higher machine availability and OEE
Fewer unplanned breakdowns
Lower repair and spares costs
Earlier detection of developing faults
Stronger evidence base for F4N assessment
Greater operator ownership and skills
PE-04e | 2
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
The 8 Pillars of TPM
TPM is built on eight supporting pillars. This guide focuses on the pillars most directly relevant to Planned Maintenance / Machine Availability: Autonomous Maintenance, Planned Maintenance, and OEE-driven Focused Improvement.
1
Autonomous Maintenance
2
Planned Maintenance
3
Focused Improvement
4
Quality Maintenance
5
Early Equipment Management
6
Training & Education
7
Safety, Health & Environment
8
TPM in Administration
Highlighted pillars are covered in this guide and in PE-04a to PE-04d.
PE-04e | 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3

## Slide 4
Measuring Performance: Overall Equipment Effectiveness (OEE)
OEE combines three factors into a single percentage that shows how effectively equipment is being used.
Availability
Actual Run Time ÷ Planned Production Time
Did it run when it should have?
x
Performance
Output Rate vs Ideal (Design) Rate
Did it run at the right speed?
x
Quality
Good Output ÷ Total Output
Did it produce good parts?
OEE = Availability x Performance x Quality
World-class benchmark: 85%. Typical unimproved batch manufacturing: 40-60%.
Target used in PE-04b OEE Dashboard and PE-04c KPI Tracker: 85%
PE-04e | 4
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4

## Slide 5
Worked Example: Calculating OEE – Step 1, Availability
Scenario: A CNC turning centre is planned to run for 160 hours this month. 3.5 hours were lost to an unplanned breakdown.
Planned Production Time
160 hrs
Downtime (unplanned)
3.5 hrs
Actual Run Time
160 − 3.5 = 156.5 hrs
Availability =
Actual Run Time
Planned Production Time
= 156.5 ÷ 160 = 97.8%
Availability of 97.8% means the asset ran for almost all of its planned time. Downtime is logged in the Breakdown & Downtime Log (PE-04b), which feeds this figure automatically.
PE-04e | 5
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 5

## Slide 6
Worked Example: Calculating OEE – Step 2, Performance
Scenario continued: The ideal cycle time means this machine should produce parts equivalent to 140 hours of output during the 156.5 hours it actually ran.
Actual Run Time
156.5 hrs
Ideal Cycle Time x Output Achieved
140 hrs equivalent
Performance =
Ideal Cycle Time x Output
Actual Run Time
= 140 ÷ 156.5 = 89.5%
Performance below 100% often points to minor stops, reduced speed running, or setup/adjustment time not captured as full breakdowns. These are good targets for Focused Improvement activity.
PE-04e | 6
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 6

## Slide 7
Worked Example: Calculating OEE – Step 3, Quality and Overall Result
Total Output
1,240 units
Good Output (passed inspection)
1,198 units
Quality = 1,198 ÷ 1,240 = 96.6%
Good output divided by total output produced
Overall OEE
OEE = Availability x Performance x Quality
= 97.8% x 89.5% x 96.6%
= 84.6%
This result (84.6%) is just below the 85% target – close to world class. The breakdown above shows Performance (89.5%) is the area with most room for improvement.
PE-04e | 7
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 7

## Slide 8
Using the OEE Dashboard (PE-04b)
The OEE Dashboard in PE-04b automates the calculation shown on the previous slides. You only need to enter four figures per asset, per month.
1
Enter Planned Production Time and Downtime (hrs)
From your production plan and the Breakdown & Downtime Log
2
Enter Ideal Cycle Time x Output (hrs equivalent)
Based on the standard/design cycle time for the part being run
3
Enter Total Output and Good Output (units)
From production records and quality inspection results
4
OEE %, breakdown and RAG status calculate automatically
Compares result to the 85% target and colours Green / Amber / Red
RAG thresholds: Green ≥ 85% | Amber 70-84% | Red < 70%
PE-04e | 8
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 8

## Slide 9
Step 1: Build Your Asset Register (PE-04b)
Every planned maintenance programme starts with knowing what equipment you have, how critical it is, and how often it needs attention.
For each asset, record:
Asset ID, name and location
Manufacturer, model and serial number
Date installed
Criticality rating (High / Medium / Low)
PM frequency (Daily to Annual)
Responsible person
Last PM date (Next PM Due calculates automatically)
Criticality drives PM frequency
High
Failure stops production, creates a safety risk, or affects product quality / nuclear safety case requirements.
Medium
Failure causes significant but contained disruption.
Low
Failure has minimal operational impact.
PM frequency bands: Daily, Weekly, Monthly, Quarterly, 6-Monthly, Annual – see PE-04a Section 6 for typical activities at each frequency.
PE-04e | 9
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 9

## Slide 10
Step 2: Generate Your 12-Month PM Calendar (PE-04b)
Once PM frequencies are set in the Asset Register, the PM Calendar gives a 12-month view of when planned maintenance is due for every asset.
Asset
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
CNC Turning Centre 1 (Weekly)
P
P
P
P
P
P
P
P
P
P
P
P
Air Compressor (Monthly)
P
P
P
P
P
P
P
P
P
P
P
P
Overhead Crane (Quarterly)
P
P
P
P
Legend: P = Planned PM due | C = Completed (green) | M = Missed / overdue (red)
Review the calendar weekly. Mark tasks ‘C’ when complete – this updates the Last PM Date and rolls the Next PM Due forward automatically.
PE-04e | 10
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 10

## Slide 11
Step 3: Introduce Autonomous Maintenance (PE-04d)
Autonomous Maintenance gives operators ownership of basic checks on their own equipment: cleaning, inspecting, lubricating and tightening. This catches developing problems early, before they cause a breakdown.
Typical daily operator checks include:
Area clear of hazards and debris
Guards, interlocks and emergency stops
Fluid levels (oil, coolant, lubrication)
Air/hydraulic pressure within range
Unusual noise, vibration or smell
Tooling and fixtures secure
Control panel free of fault codes
PE-04d provides ready-to-use check sheets for:
General Production Machine
CNC Machining Centre
Lifting Equipment (Crane / Hoist)
Compressed Air System
Monthly Extended Equipment Check
Each sheet includes a weekly sign-off record (Mon-Sun) and a training record to track who is authorised to carry out checks.
PE-04e | 11
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 11

## Slide 12
The Steps of Autonomous Maintenance (Jishu Hozen)
Autonomous Maintenance is typically introduced through a series of steps, building operator skills and equipment condition progressively.
1
Initial Cleaning
Clean equipment thoroughly; cleaning is inspection – identify and tag any defects found.
2
Eliminate Sources of Contamination
Identify and address causes of dirt, leaks and difficult-to-access areas.
3
Develop Cleaning & Lubrication Standards
Set standards and visual controls so checks are quick and consistent.
4
General Inspection
Train operators to inspect components: bolts, belts, sensors, wiring.
5
Autonomous Inspection
Operators carry out routine checks independently using the standards developed.
6
Standardise Workplace Management
Integrate checks into standard work; align with 5S and visual management.
7
Full Autonomous Maintenance
Operators take full ownership; continuously improve equipment performance.
PE-04e | 12
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 12

## Slide 13
Step 4: Record Breakdowns Consistently (PE-04b)
Every unplanned stoppage, however short, should be recorded in the Breakdown & Downtime Log. This data drives OEE, MTBF, MTTR and root cause analysis.
Record for each breakdown:
Date, time down and time back up
Asset affected
Fault description
Category of failure
Action taken / repair carried out
Person logging the entry
Failure categories
Mechanical
Electrical
Controls / PLC
Tooling
Operator Error
Material Shortage
Other
Downtime hours calculate automatically from time down/up, and totals by category feed a Pareto-style summary to focus improvement effort.
PE-04e | 13
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 13

## Slide 14
Step 5: Investigate Repeat Failures
When the same equipment fails in the same way more than twice within a rolling 3-month period, carry out a root cause analysis using established Process Improvement tools.
5 Whys
Ask ‘why’ repeatedly to move from the symptom to the underlying root cause.
Fishbone Diagram
Group potential causes under Human, Method, Machine, Materials, Equipment & Environment, and Administration.
Action tracking
Record corrective actions arising from root cause analysis in the Maintenance Improvement Action Log (PE-04c), with an owner, target date and status (Open / In Progress / Complete). Review at the monthly maintenance KPI review.
PE-04e | 14
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 14

## Slide 15
Step 6: Track KPIs Monthly (PE-04c)
The Maintenance KPI Trend Dashboard summarises performance across the site, for review at the monthly management meeting and Daily Management System (SQDCP).
PM Compliance %
Target: 95%
Higher is better
Overall OEE %
Target: 85%
Higher is better
Unplanned Downtime (hrs)
Target: 20
Lower is better
MTBF (hrs)
Target: 200
Higher is better
MTTR (hrs)
Target: 3
Lower is better
Breakdown Cost (£)
Target: 2,000
Lower is better
RAG status: Green = on target | Amber = within 10% of target | Red = off target. Trend charts show the last 12 months for each KPI.
PE-04e | 15
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 15

## Slide 16
Step 7: Manage Critical Spares (PE-04b)
A maintenance task cannot be completed on time if the right spare part is not available. The Spares & Consumables tracker helps avoid delays.
Identify critical spares for High criticality assets
Record current stock and minimum stock level
Reorder Status flags automatically when stock ≤ minimum
Track supplier, lead time and last order date
Review monthly: are lead times realistic given criticality?
Reorder Status
OK – Stock above minimum
REORDER – At or below minimum
Linked to Asset ID, so spares can be cross-referenced to the equipment they support.
PE-04e | 16
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 16

## Slide 17
Roles and Responsibilities
Clear ownership is essential for a planned maintenance programme to succeed. PE-04a defines responsibilities using a RACI model.
Production Operator
Daily autonomous maintenance checks; report abnormalities immediately
Maintenance Technician
Carry out scheduled PM tasks; respond to breakdowns; manage spares
Maintenance Manager
Own PM schedule, OEE/KPI reporting and root cause investigations
Production Manager
Resource and prioritise PM activity; review KPIs monthly
Site / General Manager
Approve capital replacement and Early Equipment Management decisions
Full RACI table covering all key activities is provided in PE-04a, Section 4.
PE-04e | 17
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 17

## Slide 18
From Reactive to Proactive: The Improvement Journey
Planned maintenance is not a one-off implementation. Data from breakdowns, OEE and KPIs should drive ongoing improvement.
Reactive
Run to failure. High unplanned downtime. No data captured.
Planned
PM schedule in place. Breakdowns logged. OEE measured.
Proactive
Operators involved (Autonomous Maintenance). Root cause analysis on repeat failures.
Predictive / Optimised
Condition monitoring. PM frequencies tuned from data. Early Equipment Management informs new equipment specs.
Use PE-04b and PE-04c data each month to identify where your site sits on this journey, and what the next priority should be.
PE-04e | 18
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 18

## Slide 19
Linking This Toolkit to F4N Assessment Evidence
Populated and used over time, the PE-04 toolkit provides direct evidence for the Planned Maintenance / Machine Availability question in the F4N Business Excellence assessment.
Maintenance schedules and PM records
PE-04a, PE-04b (Asset Register & PM Calendar)
Preventive maintenance programme
PE-04a Policy, PE-04b PM Calendar
Machine downtime and availability reporting
PE-04b (Downtime Log & OEE Dashboard), PE-04c
Evidence of corrective action following failure
PE-04c Action Log, root cause records
Operator involvement in equipment care
PE-04d Autonomous Maintenance Toolkit
PE-04e | 19
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 19

## Slide 20
Your PE-04 Toolkit at a Glance
PE-04a
Policy & Procedure
Defines the planned maintenance approach, roles and responsibilities
PE-04b
Maintenance Schedule & Asset Register
Asset register, PM calendar, downtime log, OEE dashboard, spares tracker
PE-04c
Maintenance KPI Trend Dashboard
12-month KPI trends, RAG status and improvement action log
PE-04d
Autonomous Maintenance Toolkit
Daily/weekly/monthly operator check sheets and training record
PE-04e
This Implementation Guide
Step-by-step guide to applying TPM, OEE and Autonomous Maintenance
PE-04e | 20
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 20

## Slide 21
Getting Started: First 30 Days
1
Agree scope: list all production, inspection, lifting and utility equipment to include
2
Populate the Asset Register (PE-04b) with criticality ratings and PM frequencies
3
Generate the 12-month PM Calendar and assign responsibility for each PM task
4
Introduce daily Autonomous Maintenance checks using PE-04d, starting with one or two pilot areas
5
Start logging all breakdowns in the Downtime Log, even minor stoppages
6
Calculate baseline OEE for your most critical assets
7
Set up the monthly KPI review using PE-04c and agree RAG thresholds with the team
8
Review progress after 30 days and expand Autonomous Maintenance to further areas
PE-04e | 21
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 21

## Slide 22
Common Pitfalls and How to Avoid Them
Skipping the Asset Register
Without criticality ratings, PM effort gets spread evenly instead of focused on what matters most.
Logging only major breakdowns
Small stoppages add up. Logging everything gives accurate OEE and reveals patterns.
Autonomous Maintenance without training
Operators need clear standards and training before checks become reliable.
PM Calendar not reviewed regularly
A calendar that isn't reviewed weekly quickly falls out of date and loses credibility.
KPIs reviewed but no actions taken
RAG status alone doesn't improve performance – use the Action Log (PE-04c) to close the loop.
Spares not linked to criticality
Stock-outs on critical spares cause the longest, most costly downtime.
PE-04e | 22
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 22

## Slide 23
Summary
Planned Maintenance moves equipment care from reactive to proactive, improving availability, quality and delivery
OEE (Availability x Performance x Quality) gives a single measure of equipment effectiveness against an 85% target
Autonomous Maintenance gives operators ownership of daily checks, catching issues early
PE-04a to PE-04e provide a complete, working toolkit: policy, asset register, KPI dashboard, operator checklists and this guide
Start with the Asset Register and a small Autonomous Maintenance pilot, then build out from there
PE-04e | 23
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 23