## Slide 1
A3 Problem-Solving Template
PE-07b | Process Excellence | Fit For Nuclear Toolkit
One page. The whole story. Problem to confirmed countermeasure.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
What is A3 thinking?
PE-07b
The A3 is a one-page problem-solving story, named after the paper size it was designed to fit. It forces clarity: if the problem, analysis and plan cannot be told on one page, the thinking is not yet finished. It is not a form to fill in. It is a conversation tool: the owner builds it section by section, reviews it with the team and their manager, and updates it as understanding grows. Use the A3 when a problem deserves more than a 3C entry but a full 8D would be heavyweight: recurring issues, cross-functional problems, and improvement projects.
The A3 is PDCA on a page
PLAN
Sections 1 to 4: background, current condition, target, root cause
DO
Section 5 and 6: countermeasures and implementation plan
CHECK
Section 7: follow up, measure results against the target
ACT
Standardise what works into SOPs, share the learning
Rule of thumb: spend most of your effort on the left side of the A3. A weak grasp of the problem makes every countermeasure a guess.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
A3 template
PE-07b
Title: Owner: Date: Status:
1. Background
Why does this problem matter? Link to safety, quality, delivery, cost or the CSIP. One or two sentences.
2. Current condition
What is actually happening? Go and see. Show the facts: data, sketch of the process, where the problem appears, how often, how big. No causes yet, just evidence.
3. Target condition / goal
What does good look like, by when? Make it measurable: from X to Y by date.
4. Root cause analysis
Why does the gap exist? Use 5 Whys or a fishbone (PE-04a). Show the cause chain and the evidence that verifies the root cause. Stopping at a symptom here wastes the right side of the page.
5. Countermeasures
What will remove the verified root cause? Prefer error proofing over reminders. For each countermeasure: what, who, expected effect.
6. Implementation plan
Actions, owners, dates. Small table: action / who / when / done. Include how the change will be communicated and trained.
7. Follow-up and confirmation
How and when will results be checked against the target in section 3? What did we measure? Confirmed by whom? What will be standardised into SOPs, and what learning is shared across the business?
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3

## Slide 4
A3 worked example
PE-07b
Title: Reduce final inspection bore rejects, CNC Cell 2 Owner: S. Patel Date: 06 Jan 2026 Status: Closed
1. Background
Bore diameter rejects on flange housings risk delivery to a nuclear customer and add inspection cost. Quality is a CSIP priority for 2026.
2. Current condition
3 of 25 parts rejected on 06 Jan, bore 0.04 mm oversize. Reject trend: 5 incidents in 12 weeks, all on harder material batches, all found at final inspection, none in-process. Cost so far: 14 hours rework and one delayed shipment.
3. Target condition / goal
Zero bore diameter rejects at final inspection within 8 weeks; any tool wear drift detected in-process, not at final.
4. Root cause analysis
Why oversize? Insert worn beyond limit. Why? Not changed at the right point. Why? Tool change set by elapsed time, not parts count, and harder material wears faster. Why? Tool life rules never reviewed when new materials introduced; no in-process check. Verified: worn insert from reject batch measured, wear 2x limit.
5. Countermeasures
1. Tool life by parts count per material grade (removes root cause). 2. In-process bore check at 50% of tool life (detects drift). 3. SOP-014 updated and setters briefed (sustains the change).
6. Implementation plan
Set parts-count limits per material: S. Patel, 10 Jan, done. Gauge and check sheet at machine: M. Reid, 13 Jan, done. SOP-014 revision and briefing: S. Patel, 15 Jan, done. Read across to Cells 1 and 3: J. Whitfield, 31 Jan, done.
7. Follow-up and confirmation
Checked weekly for 5 batches: zero bore rejects, two inserts changed early on in-process check (drift caught as designed). Raiser confirmed closure 17 Jan. Tool life rule standardised across all cells; learning shared at the quality clinic and SQDCP board.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4