## Slide 1
Root Cause Analysis Methods
Training Guide | PE-07c | Process Excellence
3C | 5 Whys | Fishbone | 8D | A3
Fix the cause, not the symptom, and the problem never comes back.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
Why structured problem solving matters
Firefighting feels productive. It is the most expensive way to run a factory.
PE-07c | 2
Without root cause thinking
The same problems return week after week
Fixes depend on who is on shift
Effort goes into rework, sorting and expediting
Blame replaces analysis; people hide problems
Knowledge stays in a few heads
With root cause thinking
Problems are solved once and stay solved
Everyone uses the same simple methods
Effort shifts from rework to improvement
Problems are surfaced early, without blame
Learning is captured and shared
A culture of structured problem solving is one of the clearest signs of a nuclear-ready supplier: it shows control of your processes and an appetite to improve them.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
What F4N verification looks for
Process improvement, problem-solving skills and root cause analysis training
PE-07c | 3
The F4N assessor wants to see that a culture of continuous improvement is supported by trained, engaged employees. Specifically:
1
Training carried out
Evidence that teams have been trained in structured problem solving: 5 Whys, fishbone diagrams and 8D. Training records and your skills matrix (see People Excellence) are the proof.
2
Effectively deployed
The methods are used in the real workplace, not just taught. Completed 3C charts, 5 Whys worksheets, fishbones and 8D reports in PE-04a are exactly this evidence.
3
Employees empowered
Anyone can raise a problem and join in solving it. Problems are visible on boards, owned at the right level, and the raiser confirms closure.
4
Driving improvement
Problem solving links to your KPIs (PE-03), feeds the CSIP, and the results are shared and standardised into SOPs (PE-06).
This guide gives you the methods. PE-04a gives you the working tool. Use them together and the evidence builds itself.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3

## Slide 4
Three levels of response to every problem
All three are needed. Most organisations stop after the first.
PE-07c | 4
1
Containment action
Protect the customer and the team right now.
Quarantine the batch. Make the area safe. Inform the manager. 100% inspect work in progress. Containment buys time; it fixes nothing.
2
Root cause
Find what actually caused the incident.
Go and see. Gather facts. Use 5 Whys or a fishbone to trace the cause chain. Verify the cause with evidence before acting on it.
3
Preventative action
Stop it ever happening again.
Remove or error proof the root cause. Update SOPs, PM schedules and training. Read across to similar processes. Confirm with the raiser that it worked.
If your problem log shows containment actions only, problems will keep returning. The value is in levels 2 and 3.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4

## Slide 5
Symptoms are visible. Causes are not.
Treating symptoms is like cutting a weed at ground level: it grows back.
PE-07c | 5
What you see on the shop floor (a reject, a stoppage, a late delivery) is a symptom. The cause sits below the surface, in the way the process is designed, maintained, measured or managed. Root cause analysis is simply digging down, level by level, until you reach a cause that is within your control and that, once fixed, prevents recurrence. A useful test of any proposed root cause: if we fix this, will the problem stop and stay stopped?
Visible
SYMPTOM: reject, stoppage, complaint
Direct cause: worn tool, wrong setting, missed check
Process cause: rule, method or checklist gap
System cause: how rules are set, reviewed and trained
Hidden: where the real fix lives
Dig deeper
The deeper the cause you fix, the more problems disappear with it.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 5

## Slide 6
Start with a good problem statement
A problem well stated is half solved. Use 5W2H.
PE-07c | 6
5W2H | Ask | Worked example
What | What exactly is wrong? Which defect, which failure mode? | Bore diameter 0.04 mm oversize on flange housings
Where | Where is it found? Which machine, line, site, feature? | CNC Cell 2, found at final inspection
When | When does it occur? Shift, batch, season, since when? | Morning shift, 06 Jan, harder material batches
Who | Who detected it? Who is affected? (Not who is to blame) | Final inspector; nuclear customer shipment at risk
Which | Which trend or pattern? Increasing, random, repeating? | 5th incident in 12 weeks, all on the same material
How | How was it detected? How does it differ from standard? | Bore gauge at final; in-process check does not exist
How many | How many parts, how often, how much cost? | 3 of 25 parts; 14 hours rework; one delayed shipment
Write the statement in facts and numbers. 'Quality is poor on Cell 2' invites debate; the table above invites analysis.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 6

## Slide 7
Go and see before you analyse
Problems are solved at the workplace, not in the meeting room.
PE-07c | 7
1
Go to the actual place
Stand where the problem happens. Watch the process run. Most causes reveal themselves to a careful observer within minutes.
2
Look at the actual thing
Handle the reject, the worn tool, the failed component. Keep physical evidence; do not let it be scrapped before analysis.
3
Talk to the actual people
The operator who runs the process every day usually knows more about it than anyone. Ask what changed. Listen without judging.
4
Get the actual data
Pull the check sheets, machine logs, inspection records and KPI charts (PE-03). Opinions start arguments; data ends them.
Two rules for the visit: no blame, and no solutions yet. You are there to understand, not to fix.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 7

## Slide 8
The problem-solving toolbox
Five tools, one logic: define, find the cause, fix it, prove it.
PE-07c | 8
3C Chart
Concern, Cause, Countermeasure on one line. The everyday tool for simple, single-cause problems raised at daily meetings.
Typical effort
Minutes
5 Whys
Ask why repeatedly to trace the cause chain from symptom to root. Fast, needs no forms, works anywhere.
Typical effort
Minutes to an hour
Fishbone
Team brainstorm of possible causes across 6 categories, then narrow down with evidence. Best when the cause is unclear.
Typical effort
A short workshop
8D
Eight disciplines, team-based, for major or customer-facing failures. Containment through to prevention with full records.
Typical effort
Days to weeks
A3
The whole problem story on one page: ideal for recurring issues and improvement projects. See PE-04b.
Typical effort
Days, updated live
All five live as ready-to-use working sheets in PE-04a (3C, 5 Whys, Fishbone, 8D) and PE-04b (A3).
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 8

## Slide 9
3C: Concern, Cause, Countermeasure
The fast everyday tool. One line per problem, reviewed at the daily meeting.
PE-07c | 9
CONCERN
What is wrong, in facts. A short description or a sketch.
CAUSE
The cause if it is obvious, or the immediate containment if not.
COUNTERMEASURE
The action steps, the champion who owns them, and the date.
Every 3C entry carries a category and a status:
Category (priority) | Status (lifecycle)
1 Do now, at the point of work | A Problem identified
2 Within 1 week, the team can resolve | B Countermeasure proposed and agreed
3 Within 1 week, needs external resource | C In progress, owners and targets agreed
4 Mid-term activity, plan into the CSIP | D Solved and confirmed by the raiser
Keep the chart visible at the workplace. A 3C that nobody walks past daily is a 3C that quietly dies. If a 3C entry will not close, or the cause is not obvious, escalate it to 5 Whys or a fishbone.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 9

## Slide 10
5 Whys: trace the cause chain
Each answer becomes the next question. Stop when you reach a fixable process cause.
PE-07c | 10
Why 1?
The bore was machined oversize
Why 2?
The insert was worn beyond limit
Why 3?
It was not changed at the right point
Why 4?
Tool change is set by time, not parts count
Why 5?
Tool life rules never reviewed; no in-process check
ROOT CAUSE
Ground rules
Five is a guide, not a rule: stop at the fixable process cause
Each answer must be a fact you can check, not a guess
Ask why the process allowed it, never who is to blame
Branch if there is more than one answer to a why
Do it at the workplace with the people involved
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 10

## Slide 11
5 Whys: where it goes wrong
The method is simple. The discipline is not.
PE-07c | 11
Stopping at 'operator error'
People are part of the process. If a person could make the error, the process let them. Ask why the process allowed it: missing check, unclear SOP, poor layout, inadequate training.
Stopping too early
'The insert was worn' is true and useless: changing the insert fixes one part. Keep asking why until the answer changes a rule, a method or a system.
Guessing instead of checking
Every why must be answered with evidence: measure the part, check the record, watch the process. A 5 Whys built on guesses produces a confident wrong answer.
One chain when there are two
Some problems have a cause of occurrence and a cause of escape (why it was not detected). Run a why chain for each: fix occurrence, strengthen detection.
Good test before you act: read the chain backwards using 'therefore'. If it does not flow logically, a link is missing.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 11

## Slide 12
Fishbone: map the possible causes
Also called Ishikawa or cause and effect diagram. Six branches, one effect.
PE-07c | 12
EFFECT
(the problem)
Manpower (people)
Machine
Method
Material
Measurement
Mother Nature (environment)
Small bones = individual potential causes, added by the team along each branch
Use it when the cause is genuinely unclear, when opinions differ, or when a 5 Whys keeps branching. The structure stops the team fixating on the first idea.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 12

## Slide 13
Running a fishbone session
An hour with the right people beats a week of solo analysis.
PE-07c | 13
1
Set up
Agreed problem statement (5W2H) in the head of the fish. Cross-functional team of 4 to 8, at or near the workplace, flipchart or board.
2
Brainstorm
Work branch by branch. Every idea goes up; no debating yet. Quiet voices often hold the answer: ask everyone in turn.
3
Narrow down
Team votes or scores likelihood (High / Medium / Low). Strike out causes the data already rules out.
4
Test with evidence
For each likely cause agree how to verify it: measure, inspect, trial, check records. Assign who and by when.
5
Act
Verified causes go to the Problem Register (PE-04a) with countermeasures, owners and dates. Photograph the fishbone and attach it.
The Fishbone sheet in PE-04a captures the output in a structured table, with likelihood, evidence and selection columns.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 13

## Slide 14
Verify before you act
A root cause is a hypothesis until the evidence agrees.
PE-07c | 14
Reproduce it
Can you turn the problem on and off? Run the process with and without the suspected cause. If the problem follows the cause, you have it.
Check the history
Does the cause explain the pattern? If the cause is 'harder material', rejects should align with harder batches in the records. If they do not, dig again.
Examine the evidence
Measure the worn insert, the misaligned sensor, the wrong-revision label. Physical evidence either supports the cause or it does not.
Explain the whole problem
The verified cause must account for what, where, when and how many. A cause that explains half the facts is half a cause.
In a nuclear supply chain this discipline matters doubly: corrective actions, NCR responses and 8D reports may be reviewed by your customer. Evidence-backed causes survive that review.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 14

## Slide 15
8D: team-based problem solving
For major, complex or customer-facing failures. Eight disciplines, full records.
PE-07c | 15
D0
Prepare and plan
D1
Form the team
D2
Describe the problem
D3
Interim containment
D4
Root cause analysis
D5
Choose corrective actions
D6
Implement and validate
D7
Prevent recurrence
D8
Recognise the team
When to use 8D: customer complaints and returns, safety-related failures, recurring problems that resisted simpler tools, and any nonconformance your customer asks you to formally answer. Many nuclear customers expect corrective action responses in exactly this structure.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 15

## Slide 16
8D in practice: D0 to D4
Understand and contain before you cure.
PE-07c | 16
D0 Prepare and plan
Confirm 8D is justified: significant, complex or customer-facing. Record the symptom, when first reported, and any emergency action already taken.
D1 Form the team
Small, empowered, cross-functional. A leader with authority to act, plus people who know the process, the product and the data. Name them on the report.
D2 Describe the problem
Full 5W2H plus Is / Is Not: where it occurs and where it does not, when and when not. The sharper the description, the shorter the search for the cause.
D3 Interim containment
Protect the customer immediately: quarantine, sort, 100% inspection, certified stock only. Verify containment actually works, and track its cost: that cost justifies the cure.
D4 Root cause analysis
Use 5 Whys and the fishbone. Find both the cause of occurrence and the cause of escape (why detection missed it). Verify each with evidence.
Do not let containment become the fix. Sorting and 100% inspection are a cost of failure, not a countermeasure.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 16

## Slide 17
8D in practice: D5 to D8
Cure, prevent and learn.
PE-07c | 17
D5 Choose corrective actions
Select permanent actions that remove the verified root causes. Prefer error proofing. Prove by trial that each action works and creates no new problems.
D6 Implement and validate
Put the actions in place, then measure: has the problem stopped at the customer and in-house? Only then remove the interim containment from D3.
D7 Prevent recurrence
Update SOPs (PE-06), control plans, FMEAs, PM schedules (PE-07) and training. Read across to similar parts, processes and sites: where else could this bite?
D8 Recognise the team
Close the report, capture the lessons, thank the team publicly. Recognition is what makes people volunteer for the next problem.
The 8D Report sheet in PE-04a walks through all nine disciplines with guidance beside every entry box, plus a sign-off section.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 17

## Slide 18
Choosing the right tool
Match the effort to the problem. Most problems need the simplest tool.
PE-07c | 18
Situation | Use | Why
Simple problem, cause fairly obvious, raised day to day | 3C Chart | One line, visible at the workplace, closed in days
Cause unclear but the problem is contained to one process | 5 Whys | Fast cause-chain tracing with the people involved
Cause genuinely unknown, opinions differ, several factors possible | Fishbone + 5 Whys | Structured team brainstorm, then trace the verified branch
Recurring issue or improvement project needing a managed story | A3 | One page holds the analysis, plan and follow-up together
Major failure, customer complaint, or formal response required | 8D | Team-based, fully documented, customer-recognised format
Escalate, do not restart: a 3C that will not close becomes a 5 Whys; a 5 Whys that keeps branching becomes a fishbone; a fishbone on a customer issue becomes an 8D. The work done so far carries forward.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 18

## Slide 19
Not all countermeasures are equal
The further down this list, the more your fix depends on people remembering.
PE-07c | 19
1. Eliminate
Remove the failure opportunity entirely: redesign the part, remove the step, single bin per live revision.
Strongest
2. Error proof (poka-yoke)
Make the error physically impossible or immediately obvious: fixtures that only fit one way, interlocks, counters.
3. Detect early
Catch it at the point of creation, not at final inspection: in-process checks, gauges at the machine, andon signals.
4. Warn and standardise
Visual controls, labels, updated SOPs and checklists. Useful, but relies on attention.
5. Train and remind
Briefings and retraining. Necessary to support every fix above, but never sufficient alone.
Weakest
If your standard countermeasure is 'operator briefed', expect the problem back. Aim at least one level higher every time.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 19

## Slide 20
Close the loop
A problem is not solved because an action is complete. It is solved when the result is confirmed.
PE-07c | 20
1
Verify effectiveness
Measure after the fix: did the reject rate, downtime or complaint actually stop? Compare against the target you set. Watch long enough to trust the trend.
2
Raiser confirms
Status D in PE-04a needs the person who raised the problem to agree it is gone. This protects against paper closures and builds trust in the system.
3
Standardise
Lock the fix into SOPs (PE-06), control plans, PM schedules (PE-07) and training. An unstandardised fix lasts until the next staff change.
4
Share the learning
Read across to similar processes, brief it at the communication board, log it as a lesson learned. One problem solved well can prevent ten.
The Dashboard in PE-04a tracks open items, ageing and confirmation status so nothing closes quietly.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 20

## Slide 21
Why this matters more in nuclear
Your problem-solving culture is part of your nuclear safety culture.
PE-07c | 21
Nonconformance reporting (NCR)
Nuclear customers expect every nonconformance to be reported, contained, root-caused and answered with evidence. Weak RCA in an NCR response damages credibility fast.
Counterfeit and fraudulent items (CFSI)
Suspect documentation or markings must trigger structured investigation, never a workaround. The Goods Inwards example in PE-04a shows the pattern: quarantine, investigate, fix the system gap.
A questioning attitude
Nuclear safety culture asks everyone to challenge anomalies and raise concerns. A no-blame problem-solving system is the practical machinery that makes a questioning attitude safe to have.
Conservative decision making
When the cause is uncertain, contain and investigate; never assume and ship. Documented RCA gives you the evidence base for sound, defensible decisions.
See the Nuclear Awareness category of the toolkit for full guidance on safety culture and CFSI.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 21

## Slide 22
Embedding problem solving in daily life
Tools sit in drawers. Routines change cultures.
PE-07c | 22
1
Daily SQDCP meeting
Every red day on the board gets a 3C entry before the meeting ends. The board surfaces the problem; the 3C makes someone own it. (See PE-03.)
2
Weekly quality clinic
A short standing review of open problems: ageing items, repeat causes, stuck countermeasures. The Dashboard in PE-04a is the agenda.
3
Train through doing
Run the first 5 Whys and fishbones with a facilitator, on real problems. Record who has taken part in your skills matrix so coverage is visible.
4
Make it safe to raise problems
Thank the raiser publicly. Track time-to-close, not number-raised. The moment raising a problem becomes a risk, the problems go underground.
Aim for rhythm over heroics: a steady flow of small problems solved beats an annual improvement blitz.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 22

## Slide 23
Summary and getting started
Everything you need is in PE-04a and PE-04b. Start this week.
PE-07c | 23
Seven habits of root cause thinking
Every problem gets three responses: contain, root cause, prevent
Define the problem with 5W2H, in facts and numbers, before analysing
Go and see: place, thing, people, data
Match the tool to the problem: 3C, 5 Whys, Fishbone, A3, 8D
Verify the root cause with evidence before acting
Choose countermeasures high on the hierarchy: error proof, do not remind
Close the loop: confirm with the raiser, standardise, share
Your first steps
Open PE-04a and log your five most recent problems in the Problem Register
Put a 3C chart up at one workplace and review it at the daily meeting
Run one facilitated 5 Whys on a real, current problem with the team involved
Pick one recurring problem and run it as a fishbone workshop
Review the Dashboard at your next management meeting and agree owners for anything ageing
Solve the problem once, learn from it forever.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 23