## Slide 1
Traceability, Non-Conformance
and CFSI
Understanding your responsibilities in the nuclear supply chain
Commercial in Confidence
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
Why Traceability, NCR, and CFSI Matter
These three areas are deeply linked. Together they are the backbone of nuclear supply chain quality assurance. Getting them right protects safety, your company, and your customers.
TRACEABILITY
Every component in a nuclear facility must be traceable to its origin. Without traceability, you cannot prove what you supplied or confirm it meets specification. A broken traceability chain can result in rejection of completed work.
NON-CONFORMANCE
Non-conformances happen in every manufacturing environment. The question is not whether they occur, but whether they are identified, controlled, and closed properly. Uncontrolled NCs are a serious risk.
CFSI
A counterfeit or fraudulent item in a nuclear application can cause a safety event. Preventing CFSI entering the supply chain is a collective responsibility shared across every person in every tier.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
Traceability: What It Means and Why It Is Required
Traceability means being able to reconstruct the complete history of any item: from the raw material source, through every manufacturing process, inspection, and test, to the finished product delivered to the customer.
What must be traceable:
Raw material: to heat/batch number and certificate
Every manufacturing operation: signed traveller
Every inspection and test: signed ITP / job card
Any non-conformances: NCR reference
Offcuts retained for use: yellow offcut tag
Final delivered item: to its Lifetime Quality Record
The traceability chain:
RAW MATERIAL
Material cert: grade, heat no., mechanical properties
GOODS RECEIPT
Cert verified, CFSI check, ID applied, register updated
MANUFACTURE
Traveller signed at every operation
INSPECTION
ITP activities signed off at each hold/review point
FINAL RELEASE
LQR complete; Certificate of Conformity issued
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3

## Slide 4
Your Traceability Responsibilities
Goods In
Verify cert matches PO spec. Apply ID immediately. Update material register. CFSI check on every delivery.
Never receive material without a certificate. Never store material without identification.
Production
Keep the traveller with the job at all times. Sign and date at every operation. Never remove ID from WIP. Tag offcuts before moving them.
A part without a traveller is an unknown part. Stop work and notify QM.
Inspector
Verify traceability at every ITP hold/review point. Check heat number matches cert before signing. Quarantine anything with broken traceability.
If traceability cannot be verified, the part fails the inspection point.
Despatch
Check LQR is complete before releasing. Confirm CoC is signed. Include all specified traceability documents in the delivery.
Never release a delivery without a signed CoC and complete documentation.
Everyone
If you see material without identification, tell your supervisor. If a job card goes missing, stop the job and tell QM. Never use unidentified material.
Broken traceability discovered at the customer is far more costly than stopping to fix it now.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4

## Slide 5
Offcut and Remnant Material Control
Offcut control is one of the most commonly failed elements during nuclear customer audits and site tours. An unidentified offcut in the store is an immediate non-conformance.
The rule is simple:
When you cut material
Apply a yellow offcut tag to the offcut BEFORE you move it. The tag must show: heat number, material grade, certificate reference, original item reference, date cut, your name.
Small offcuts not worth keeping
Scrap them immediately. Do not put them in the store unlabelled. An unlabelled piece of material in the store is a problem waiting to happen.
Offcuts going back into store
Log them in the Offcut Register as a new entry, cross-referenced to the original material entry.
If you find an unlabelled offcut
Quarantine it. Tag it as UNKNOWN MATERIAL. Tell your supervisor. It cannot be used for any nuclear-classified work until its identity is verified.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 5

## Slide 6
What Are CFSI Items?
Counterfeit, Fraudulent, and Suspect Items (CFSI) are a real and growing threat in global supply chains. They are especially dangerous in safety-critical applications.
COUNTERFEIT
Items intentionally made to imitate genuine products without authorisation. Examples: reprocessed scrap parts stamped as new; bolts made from lower-grade material and stamped with a higher grade; items with copied markings.
FRAUDULENT
Genuine items supplied with false or altered documentation. Examples: a Type 2.1 certificate altered to read Type 3.1; welding certificates showing qualifications the welder does not hold; NDT reports for tests that were never carried out.
SUSPECT
Items where there is reason to believe they may not be genuine. They have not yet been confirmed as counterfeit, but must be treated as non-conforming until proven otherwise.
GREY MARKET
Genuine items sourced outside the OEM's authorised distribution network. May be real but: wrong revision, out of shelf life, improperly stored, documentation unverifiable. Unacceptable for QC1/QC2 without QM approval.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 6

## Slide 7
CFSI Warning Signs: Purchasing
If any of these apply when you are sourcing a component, stop and tell the Quality Manager before placing an order.
1. Price significantly below normal market price
If it's too good to be true, it probably is.
2. Obsolete or hard-to-get item suddenly available
Counterfeiters target items that are no longer made.
3. Shorter lead time than expected from a new supplier
Genuine items need manufacture time. Pre-stocked fakes do not.
4. Unfamiliar or unusual supplier for a critical item
Use approved suppliers only. New sources for safety-classified items need QM approval.
5. Supplier cannot provide OEM authorisation or distributor status
Legitimate nuclear supply chains are documented and verifiable.
6. Item not available from OEM's authorised distribution
Grey market = unverifiable chain of custody for QC1/QC2.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 7

## Slide 8
CFSI Warning Signs: Goods Receipt
Every goods receipt inspection must check for these signs. If any are present, quarantine the items and notify the Quality Manager.
Paperwork
Poor spelling/grammar; Tipp-Ex or alterations; missing info; typed/image signatures where wet signatures expected
Certification
Certificate does not cross-reference to the item; heat/batch number inconsistent; specification superseded; unrecognised test body
Packaging
Different from previous deliveries of the same item; unusual labels; signs of repackaging or tampered seals
Product Condition
Evidence of reworking, repainting, or restamping; unexpected wear or surface condition; repairs not documented
Identification Marks
Alterations to markings; missing lot/batch numbers; smudged or blurred text; incorrect logo; wrong marking method
Item Appearance
Different colour, weight, shape, or size from previous deliveries; wrong thread profile; obvious dimensional discrepancies
Documentation Mismatch
Drawing revision differs from order; subtle part number difference; quantity or description inconsistency
OEM Certification Missing
Original Equipment Manufacturer certification unavailable or unverifiable; supplier cannot trace item to OEM
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 8

## Slide 9
CFSI: What to Do If You Suspect an Item
This is the most important thing you can do: ACT IMMEDIATELY. Do not wait, do not assume it will be fine, do not tell yourself 'it's probably OK'.
1. STOP
Stop using the item and any others from the same batch or delivery. Right now.
2. TAG IT
Apply a red CFSI SUSPECT tag to the item. This prevents anyone else using it.
3. QUARANTINE
Move the item to the CFSI Quarantine store. The store must be locked.
4. PHOTOGRAPH
Photograph the item, packaging, all markings, and all documents.
5. NOTIFY QM
Tell the Quality Manager within 30 minutes. Provide: item, batch no., supplier, date received, what you saw.
6. DO NOT RETURN
Do not return the item to the supplier. This destroys evidence.
7. WAIT
The QM will raise a CFSI report, notify the customer, and start the investigation.
8. PRESERVE
Keep all original packaging with the quarantined item until told otherwise by QM.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 9

## Slide 10
Non-Conformance Reports (NCR): The Basics
A Non-Conformance Report is raised when any product, material, service, or activity does not meet the specified requirements. Raising an NCR is not a sign of failure. It is a sign of a professional, controlled quality system.
When must you raise an NCR?
Dimensions or surface condition outside drawing tolerance
Material certificate does not meet the specification
Weld defects identified during visual or NDT inspection
Traceability has been broken and cannot be re-established
Any CFSI suspect item
Work has proceeded past a hold point without sign-off
A procedure has not been followed correctly
Customer reports a quality issue on a delivered item
What you must NOT do:
Continue working on a non-conforming item without a disposition
Scrap a non-conforming item without QM approval (destroys evidence)
Rework an item without QM approval (may invalidate documentation)
Accept a non-conforming item informally without raising an NCR
Send a non-conforming item to the customer
NCRs generate evidence. Evidence protects you. A company that can produce clean NCR records with closed corrective actions scores higher at F4N assessments and customer audits than one with no NCRs at all.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 10

## Slide 11
NCR: The Process and Disposition Options
The NCR process:
1. IDENTIFY
Non-conformance found
2. STOP
Segregate the item
3. RAISE NCR
Within 1 hour
4. NOTIFY QM
Immediately
5. CUSTOMER NOTIFY
Within 24hrs (QC1/QC2)
6. ASSESS ROOT CAUSE
QM leads
7. AGREE DISPOSITION
QM + customer if needed
8. CLOSE
Evidence filed
Disposition options:
REWORK
Bring back to full specification. No customer approval needed.
REPAIR
Cannot be brought to full spec but can be repaired. CUSTOMER APPROVAL REQUIRED.
USE AS IS
Accept in non-conforming state. CUSTOMER APPROVAL REQUIRED.
SCRAP
Destroy. Cannot be reworked or accepted. Must be documented.
RETURN TO SUPPLIER
Only after QM authorisation. Evidence preserved first.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 11

## Slide 12
Your Traceability, NCR and CFSI Toolkit
These documents work together as a complete system. Use them on every job.
QHSE-TNC-01
Material and Product Traceability Procedure
Defines how materials are received, identified, tracked through manufacture, and released. The rules everyone must follow.
QHSE-TNC-02
Traceability and WIP Register
Material Register, WIP Traveller Log, Offcut Register, Quarantine Log, and Goods Receipt Inspection Record. Live operational tools.
QHSE-TNC-03
NCR Log and NCR Form
The NCR form to raise and the log to track all non-conformances, root cause analysis, corrective actions, and concessions.
QHSE-TNC-04
CFSI Procedure and Awareness Guide
Full CFSI definitions, warning signs, response procedure, preventive controls, and CFSI incident register.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 12

## Slide 13
Traceability, NCR, and CFSI
Three things to remember:
1. If material has no ID, quarantine it. 2. If something is wrong, raise an NCR. 3. If something looks like CFSI, quarantine it and tell the Quality Manager.
Questions? Ask your supervisor or the Quality Manager.
Commercial in Confidence | [Company Name] | [Date]
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 13