## Slide 1
KNOW THE WARNING SIGNS
COUNTERFEIT, FRAUDULENT AND SUSPECT ITEMS (CFSI) | IF IN DOUBT — STOP AND TELL THE QUALITY MANAGER
AT PURCHASING — RED FLAGS
AT GOODS RECEIPT — RED FLAGS
1. Price significantly lower than normal market price If it's too good to be true, it probably is.
2. Obsolete or hard-to-get item suddenly available Counterfeiters target items no longer in production.
3. Shorter lead time than expected Pre-stocked fakes don't need manufacture time.
4. Unfamiliar or new supplier for a critical item Use the Approved Supplier List only.
5. Supplier cannot prove OEM authorisation Legitimate nuclear suppliers have documented traceability.
6. Item sourced outside OEM distribution (grey market) Unacceptable for QC1/QC2 without QM approval.
1. Paperwork: poor spelling, alterations, Tipp-Ex, missing info Legitimate documents are clean and complete.
2. Certificate: hand-written changes, not traceable to item, superseded standards Check heat/batch number matches the physical item.
3. Packaging: different from previous deliveries of same item Photograph differences and notify QM.
4. Product condition: evidence of reworking, new paint, unexpected wear New items should look new.
5. Identification marks: altered, smudged, missing lot numbers, wrong logo Compare with previous genuine deliveries.
6. Item appearance: wrong colour, weight, size, or thread form If it looks different — stop and check.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
NON-CONFORMANCE REPORTS (NCR)
WHAT TO DO WHEN SOMETHING GOES WRONG | A non-conformance is anything that does not meet the specified requirement
ALWAYS RAISE AN NCR WHEN:
1
Dimensions are outside drawing tolerance
2
Material certificate does not match specification
3
Weld defects found during visual or NDT inspection
4
Traceability is broken and cannot be re-established
5
A CFSI suspect item is identified
6
Work has passed a hold point without proper sign-off
7
A procedure has not been followed
8
Customer reports a quality issue with your delivery
WHAT TO DO — IN ORDER:
STOP
Stop work on the affected item immediately.
SEGREGATE
Physically separate the NC item from conforming work.
TAG
Apply a RED Non-Conforming Item tag to the item.
NOTIFY QM
Tell the Quality Manager within 1 hour.
RAISE NCR
Complete the NCR form in QHSE-TNC-03.
CUSTOMER
QM notifies customer within 24hrs for QC1/QC2.
WAIT
Do not rework, scrap, or release without QM written disposition.
CLOSE
Corrective action completed and verified by QM.
NEVER DO THIS:
✕
Continue working on a NC item without a disposition
✕
Scrap a NC item without QM approval (destroys evidence)
✕
Rework without QM approval
✕
Accept a NC item informally without raising an NCR
✕
Send a NC item to the customer
✕
Pressure colleagues not to raise NCRs
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
TRACEABILITY RULES
EVERY ITEM MUST BE IDENTIFIABLE AT ALL TIMES | No ID = Quarantine
GOODS IN
Verify the material certificate matches the specification BEFORE accepting delivery.
Apply identification to every item immediately. Log in the material register.
Carry out CFSI inspection on every delivery.
MATERIAL STORE
Every item in the store must have its identification visible.
Different grades MUST be stored separately.
If you find something with no ID: quarantine it and tell your supervisor.
OFFCUTS
Apply a YELLOW OFFCUT TAG before moving any offcut.
Tag must show: heat number, grade, cert reference, original job, date cut, your name.
Small offcuts not worth keeping: scrap immediately. Never store unlabelled.
PRODUCTION
The traveller or job card must stay with the part at all times.
Sign and date at every operation.
Never remove identification markings from WIP.
If the traveller goes missing: STOP and tell the Quality Manager.
INSPECTION
Verify the heat/batch number on the material against the certificate at every ITP hold point.
Do not sign off traceability you cannot verify.
Quarantine anything where traceability is broken.
DESPATCH
Check the LQR is complete before releasing any item.
CoC must be signed by the Quality Manager.
Do not despatch any item without a signed Certificate of Conformity.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3