## Slide 1
QHSE Training Guide
COSHH Awareness
for Employees
Understanding hazardous substances, your rights and responsibilities, and how to protect yourself and your colleagues every day.
Aligned to: COSHH Regulations 2002 | HSG97 | ISO 45001:2018 | EH40 Workplace Exposure Limits
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1
Notes: Welcome participants. This training covers COSHH Regulations 2002 as they apply to day-to-day work in manufacturing and engineering. It is for all employees who work with, near, or are potentially exposed to hazardous substances.

## Slide 2
What You Will Learn
Learning Objectives
What COSHH is and why it applies to your work
What counts as a hazardous substance and where to find them in your workplace
How hazardous substances can enter your body and the harm they cause
How to find and read your COSHH assessment and Safety Data Sheet
The controls that protect you and your responsibilities in using them correctly
How to select and use PPE correctly for hazardous substance work
What health surveillance means and why your participation matters
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2
Notes: Run through objectives. Ask who has read a COSHH assessment or SDS before. Most people will say they have seen one but cannot recall what was in it. This training changes that.

## Slide 3
The Law
What is COSHH and Why Does It Exist?
COSHH stands for the Control of Substances Hazardous to Health. The COSHH Regulations 2002 (as amended) are the main piece of UK law that governs how employers and employees manage exposure to hazardous substances in the workplace. They exist because occupational exposure to hazardous substances kills and seriously harms thousands of workers every year.
1
Employer duty to assess
Every employer must identify hazardous substances used at work and carry out a COSHH assessment for each one before work begins. The assessment must evaluate who is at risk and how.
2
Employer duty to control
Employers must put in place adequate controls to prevent or adequately control exposure. Controls must follow the hierarchy: elimination first, PPE last. Controls must be maintained and tested.
3
Employee duty to cooperate
You are legally required to follow the controls in your COSHH assessment, use PPE correctly, report concerns, and attend health surveillance when arranged. This is not optional.
4
Health surveillance
Where COSHH assessments identify a risk of specific health effects, employers must arrange health surveillance. You have the right to access your own health surveillance records.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3
Notes: Stress that COSHH applies to ALL hazardous substances, not just obviously dangerous chemicals. Cutting fluids, welding fume, wood dust, cleaning products, lubricants and aerosols all fall under COSHH.

## Slide 4
Identifying Hazards
What Counts as a Hazardous Substance?
A hazardous substance is any substance (solid, liquid, gas, vapour, dust, fume, or mist) that is capable of causing harm to health. In manufacturing and engineering, they are everywhere.
Chemicals
Solvents, acids, alkalis, adhesives, lubricants, hydraulic fluids, cutting oils
Dusts & Fumes
Metal dust, wood dust, welding fume, grinding dust, paint mist, flour dust
Natural substances
Latex, flour, biological agents, mould, animal matter, bacteria in coolant
Biological agents
Legionella in water systems, MWF bacteria, blood-borne viruses if first aiding
Nanomaterials
Some advanced manufacturing processes generate nano-scale particles with unknown health effects
Carcinogens
Welding fume (Group 1), hardwood dust, mineral oils (prolonged skin contact), silica dust
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4
Notes: Challenge participants: can they name three hazardous substances they use in their area? Can they tell you where the COSHH assessments are held for those substances?

## Slide 5
Routes of Entry
How Hazardous Substances Enter Your Body
Understanding how substances enter the body is essential to understanding why the correct controls matter. A substance cannot harm you unless it gets inside you. The four routes below are the primary entry points in a manufacturing environment.
Inhalation
Breathing in
~80%
of cases
By far the most common route in manufacturing. Vapours, fumes, mists, dusts, and gases are inhaled directly into the lungs. Effects can be immediate (irritation, dizziness) or develop over years (asthma, fibrosis, cancer).
Skin Absorption
Through the skin
~15%
of cases
Many solvents and chemicals pass directly through the skin without any visible sign of entry. Repeated skin contact with cutting fluids causes dermatitis. Organic solvents can pass through to the bloodstream.
Eye Contact
Splash or vapour
Splashes of liquid chemicals or airborne particles cause immediate eye damage. Some vapours cause chronic eye irritation with prolonged exposure. Eye contact can also allow substances to enter the bloodstream via the lacrimal system.
Ingestion
Swallowing
~5%
of cases
Accidental ingestion from contaminated hands. Eating, drinking, or smoking in work areas. Touching the face with contaminated hands. This route is almost entirely preventable through good hygiene practices.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 5
Notes: Inhalation is the route workers most underestimate because you cannot see what you are breathing. Fumes from welding or grinding can look minimal in a large workshop but still exceed Workplace Exposure Limits at the breathing zone.

## Slide 6
Health Effects
Acute vs Chronic Health Effects
The timing of health effects from hazardous substances varies enormously. Some are immediate and obvious. Others develop silently over years before any symptoms appear. Chronic effects are often irreversible by the time they are diagnosed.
ACUTE EFFECTS — Immediate or Short-Term
Irritation of eyes, nose, throat, or skin — often within seconds of exposure
Dizziness, nausea, or headache from solvent or fume inhalation
Chemical burns to skin or eyes from acid or alkali contact
Breathing difficulties from high concentration fume or gas inhalation
Metal fume fever from inhalation of zinc or other metal oxide fumes when welding galvanised steel
CHRONIC EFFECTS — Long-Term or Latent
Occupational asthma from sensitisation to isocyanates, MWF, or welding fume
Occupational dermatitis from repeated skin contact with oils, solvents, or chemicals
Cancer from long-term exposure to carcinogens such as welding fume or mineral oils
Silicosis, asbestosis, or other occupational lung diseases from dust exposure
Neurological damage from chronic solvent or heavy metal exposure over many years
Critical point: Chronic occupational diseases typically have a latency period of 5-40 years. By the time a worker is diagnosed with occupational asthma or lung cancer, the damage from exposures decades earlier is irreversible.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 6
Notes: Occupational asthma is a particularly important example. Once sensitised, a person may react to concentrations of the substance so low that they cannot be detected. They can never return to that type of work environment. Sensitisation is permanent.

## Slide 7
Safety Data Sheets
Reading a Safety Data Sheet (SDS)
Every hazardous substance supplied for use at work must have a Safety Data Sheet (SDS) provided by the supplier. An SDS has 16 mandatory sections. You do not need to read all 16 in detail — but you must be able to find the sections that matter for your job.
1
Identification
Product name, supplier, emergency contact
2
Hazard Identification
GHS classification, hazard statements (H-codes)
3
Composition
Ingredients and concentrations
4
First Aid Measures
What to do if exposed — CRITICAL for emergencies
5
Fire-Fighting Measures
Extinguisher types, hazardous combustion products
6
Accidental Release
Spill procedure, containment, disposal
7
Handling and Storage
Safe use conditions, incompatibilities
8
Exposure Controls / PPE
WEL values, required PPE specifications
11
Toxicological Information
Acute toxicity, skin/respiratory sensitisation
15
Regulatory Information
REACH, specific regulations applicable
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 7
Notes: Bring an actual SDS from the workplace to this slide. Walk through finding Section 4 (first aid) and Section 8 (PPE/WEL). Ask who knows where SDSs are kept at the point of use. Many workers will say they exist but cannot locate them quickly.

## Slide 8
Your COSHH Assessment
What Your COSHH Assessment Tells You
Your employer must produce a COSHH assessment for every hazardous substance you work with. This is not a tick-box document. It is your specific protection plan for that substance in your workplace. You must read it before working with the substance.
What the substance is
Product name, chemical name, SDS reference, hazard classification
What task you are using it for
The specific operation, machine, or process the assessment covers
Who is at risk
Which job roles or groups could be exposed, including bystanders
How you might be exposed
Which routes of entry are relevant: inhalation, skin, ingestion
What the health effects are
Both acute and chronic effects specifically relevant to this substance
What controls are in place
Engineering controls (LEV), admin controls (SOPs), health surveillance
What PPE you must wear
Specific PPE type, standard rating, and when it is required
What to do in an emergency
Spill procedure, first aid, emergency contacts
When it was assessed and reviewed
Assessment date, assessor name, and next review date
When it was assessed and reviewed
Assessment date, assessor name, and next review date
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 8
Notes: At this point, ideally distribute printed COSHH assessments for substances used in the participants' area. Ask them to find the PPE section and the emergency procedure. Many will struggle, which reinforces why training is needed.

## Slide 9
Control Hierarchy
Controlling Exposure: The Right Order
COSHH Regulation 7 requires employers to prevent exposure to hazardous substances, or where that is not reasonably practicable, to adequately control it. Controls must be applied in this order. PPE is always the last resort — not the first response.
1. ELIMINATION | Most Effective
Remove the hazardous substance completely. Can the process be redesigned so the substance is no longer needed? Example: water-based adhesive replacing solvent-based.
2. SUBSTITUTION
Replace with a less hazardous substance or form. Example: soluble cutting oil with a lower sensitisation potential. Water-miscible paint instead of solvent-borne.
3. ENGINEERING CONTROLS
Physical controls to contain or extract the substance. Local Exhaust Ventilation (LEV), total enclosure, wetting down of dusts, enclosed processes. Must be maintained and tested.
4. ADMINISTRATIVE CONTROLS
Reduce exposure through how work is organised. Limit duration of exposure, rotate workers, restrict access to areas, safe systems of work, good supervision, training.
5. PPE | Least Effective
Respiratory Protective Equipment, gloves, aprons, eye protection as the final layer of protection. Must be the correct type, properly fitted, maintained, and consistently worn.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 9
Notes: The most common failure mode in COSHH is jumping straight to PPE without considering whether engineering controls or substitution could be used. LEV is dramatically more effective than RPE at source control.

## Slide 10
Engineering Controls
Local Exhaust Ventilation (LEV): Your Primary Defence
Local Exhaust Ventilation (LEV) is the most important engineering control for airborne hazardous substances in manufacturing. When designed, positioned, and maintained correctly, LEV captures fume, dust, or vapour at the point of generation before it enters the breathing zone. It only works if it is used correctly every time.
Using LEV Correctly
Position the extraction hood within the specified distance of the source (typically within 100-300mm for welding LEV)
Switch LEV on before starting work and leave it running for a period after work stops to clear residual fume
Check the face velocity and airflow indicator before starting work if one is fitted
Report any signs of reduced airflow, unusual noise, or visual signs of fume escaping to your supervisor
Never block or redirect LEV ductwork with materials, equipment, or other obstructions
Common LEV Mistakes
Hood too far from source — fume escapes before being captured
Working on the wrong side of the extraction — fume drawn across the breathing zone
LEV switched off to save time before work is complete
Ductwork blocked, kinked, or disconnected reducing airflow substantially
Assuming LEV is working because it makes noise — flow must be verified
Legal requirement: LEV systems must be examined and tested by a competent person at least every 14 months under COSHH Regulation 9. Records must be kept for at least 5 years. Employers must not use LEV known to be faulty.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 10
Notes: COSHH Regulation 9 is specific about LEV testing. Many SMEs are non-compliant because they do not have LEV examination records. This is a common finding on F4N verification visits when the QHSE evidence is reviewed.

## Slide 11
PPE for COSHH
Selecting and Using PPE for Hazardous Substances
When engineering and administrative controls are not sufficient alone, PPE provides the final layer of protection. The COSHH assessment specifies exactly which PPE is required for each substance. Generic PPE does not provide adequate protection. Specification matters.
Respiratory Protective Equipment (RPE)
FFP2 or FFP3 disposable masks are not equivalent. FFP3 required for carcinogens. Half-face with P3 filter for dusts/particulates. OV (organic vapour) cartridge for solvents. Face fit test required for tight-fitting RPE. Check expiry dates on disposable masks.
Gloves
Different materials protect against different chemicals. Nitrile for oils and solvents. Neoprene for acids. Latex avoided where skin sensitisation risk exists. Check EN374 chemical resistance standards. Gloves have breakthrough times — check the SDS and do not exceed them.
Eye and Face Protection
Safety glasses alone do not protect against splashes. Chemical splash goggles (indirect venting) required where splashing risk exists. Face shield required for transfer of bulk hazardous liquids. UV-blocking visor mandatory for welding. Check EN166 classification.
Skin and Body Protection
Chemical-resistant apron or lab coat for splashing risk. Full coverall for total enclosure entry or high contamination tasks. Ankle boots or wellingtons for floor-level chemical risk. Replace items that become contaminated — do not continue wearing.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 11
Notes: Face fit testing is a legal requirement for all tight-fitting RPE (half-face, full-face respirators). Many SMEs issue RPE without conducting face fit tests. This renders the RPE legally and practically ineffective. Facial hair prevents an adequate seal.

## Slide 12
Skin Protection
Protecting Your Skin: Dermatitis is Preventable
Occupational skin disease, primarily contact dermatitis, is one of the most common occupational health conditions in manufacturing. It is also almost entirely preventable. Once skin becomes sensitised to a substance, even tiny amounts can trigger a reaction for the rest of a person's working life.
The Skin Care Routine: Three Steps
1
BEFORE work
Apply barrier cream to clean, dry skin BEFORE putting on gloves or starting work. Barrier cream is not a substitute for gloves — it works alongside them. Apply to hands, wrists, and any other exposed skin.
2
DURING work
Wear nitrile gloves as specified in the COSHH assessment. Remove and replace gloves if they become contaminated inside, torn, or show signs of chemical breakthrough (discolouration, softening).
3
AFTER work
Wash with warm water and a mild, pH-neutral soap. Do not use solvents or harsh abrasives to clean your skin. Dry thoroughly with a clean towel. Apply moisturising cream after washing to restore skin barrier function.
Warning Signs: Report These Immediately
Redness, itching, or dry and cracked skin on hands or forearms
Blisters, swelling, or weeping sores on the skin after chemical contact
Skin that remains inflamed even at weekends or during holiday periods
Breathing difficulties, cough, or wheeze that worsens during or after work
Eye irritation, watering, or redness that occurs during the working day
Do not wait: Report any of the above symptoms to your supervisor or occupational health contact immediately. Early intervention almost always prevents permanent sensitisation. Delaying report allows permanent damage to develop.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 12
Notes: Emphasise that reporting symptoms early is crucial. Many workers tolerate symptoms thinking they will go away. By the time they report, sensitisation has occurred and the condition is permanent. The reporting obligation is theirs, and the legal duty to act is the employer's.

## Slide 13
Health Surveillance
Health Surveillance: Your Right and Your Protection
Where the COSHH assessment shows there is a reasonable likelihood that a substance could cause identifiable disease or health effects, COSHH Regulation 11 requires the employer to carry out health surveillance. Health surveillance is designed to detect early signs of harm before they become serious.
Skin surveillance
Quarterly
Regular visual inspection of hands, wrists, and forearms by a trained person. Identifies early dermatitis. Required for workers exposed to metalworking fluids, cutting oils, solvents, and epoxy resins.
Respiratory surveillance
Annual
Annual lung function test (spirometry) for workers exposed to respiratory sensitisers including welding fume, isocyanates, wood dust, and flour. Baseline test on first exposure.
Audiometric testing
Annual
Pure tone audiometry for workers in hearing protection zones or exposed to noise above 85 dB(A). Detects early hearing loss from noise exposure.
Health questionnaire
Annual
Structured questionnaire asking about respiratory, skin, and general health symptoms. Can identify early sensitisation before clinical signs appear. Completed before first exposure and annually.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 13
Notes: Health surveillance records must be retained for 40 years for substances that cause chronic disease with long latency periods. This allows future diagnosis to be linked to past exposure. Employers must not disclose individual results without consent.

## Slide 14
Emergencies
What to Do in a COSHH Emergency
COSHH Regulation 13 requires employers to prepare procedures for accidents, incidents, and emergencies involving hazardous substances. Every employee must know the immediate actions for the substances they work with. Do not wait until an emergency to find out.
Skin Contact
Remove contaminated clothing immediately
Wash skin with large quantities of water for at least 15 minutes
Check SDS Section 4 for specific first aid guidance
Seek medical attention if irritation persists or substance is severely corrosive
Report to supervisor and complete incident report
Eye Contact
Irrigate eye immediately with clean water for at least 15 minutes
Use the nearest eyewash station — they must be accessible within seconds
Hold eyelids open during irrigation to ensure full flushing
Do not rub the eye
Seek medical attention immediately for all chemical eye contacts
Inhalation
Remove person from the exposure area to fresh air immediately
Loosen any tight clothing around the neck or chest
If unconscious or not breathing, call 999 and start CPR
Do not re-enter a contaminated atmosphere without RPE
Seek medical attention — symptoms may be delayed for several hours
Spill
Evacuate personnel from the immediate area
Ventilate the area if safe to do so without creating further exposure
Use spill kit materials specified for the substance — know where they are
Do not use absorbent materials that may react with the spilled substance
Do not allow entry to clean up without correct PPE and training
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 14
Notes: Ask participants: where is the nearest eyewash station to your work area? Could you reach it within 10 seconds with your eyes shut? Many cannot. The COSHH Regulations require eyewash to be immediately accessible, not just available somewhere on site.

## Slide 15
Hygiene
Workplace Hygiene: Simple Actions that Prevent Serious Harm
Many occupational health conditions caused by hazardous substances are preventable through basic hygiene measures. These are simple, cost nothing, and can prevent irreversible harm. They are also a legal requirement under the Workplace (Health, Safety and Welfare) Regulations 1992.
Good Practice — Always Do These
Always wash hands before eating, drinking, or visiting the toilet after working with hazardous substances. Use warm water and mild soap. Dry thoroughly.
Never eat, drink, chew gum, or smoke in areas where hazardous substances are used or stored. Ingestion is a preventable route of entry.
Keep contaminated clothing separate from clean clothing. Change clothing if significantly contaminated. Do not take contaminated PPE or workwear home.
Apply moisturising cream after washing hands at end of shift. This restores the skin barrier and dramatically reduces dermatitis risk.
Report any leaks, spills, or substance releases to your supervisor immediately, even if they appear minor. Small exposures add up over time.
Common Mistakes — Never Do These
Never use solvents, thinners, or any hazardous substance to clean your skin. This removes protective oils and introduces chemicals directly through the skin barrier.
Do not ignore safety data sheets, COSHH assessments, or hazard labels because you have used the substance for years without apparent harm. Chronic effects develop slowly.
Do not decant substances into unmarked containers. Always keep hazardous substances in their original, correctly labelled container.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 15
Notes: Hygiene is the most underrated control in COSHH. Workers who handle cutting fluids all day but wash their hands before eating dramatically reduce their ingestion risk. This slide should generate discussion about current habits.

## Slide 16
Your Workplace
Common Substances in Manufacturing: Know the Risks
The following are the substances most frequently associated with occupational health conditions in engineering and manufacturing. Each is common, each is hazardous, and each is manageable with the right controls.
Metalworking Cutting Fluids (MWF)
Risk: Dermatitis, occupational asthma, hypersensitivity pneumonitis
Controls: Concentration monitoring, sump hygiene, gloves, barrier cream, skin surveillance quarterly
Welding Fume (all types)
Risk: Lung cancer (Group 1 carcinogen), manganism, COPD, metal fume fever
Controls: LEV at source within 300mm, RPE (P3 minimum) when LEV marginal, no compressed air to clear fume
Solvents (IPA, acetone, thinners)
Risk: CNS effects, dermatitis (defatting), liver damage with chronic exposure
Controls: Enclosed processes, MEL/WEL monitoring, OV cartridge RPE, no skin cleaning with solvents
Silica Dust (grinding, cutting)
Risk: Silicosis (irreversible fibrosis), lung cancer, COPD
Controls: Wet suppression, LEV, FFP3 RPE, no dry sweeping, WEL 0.1 mg/m3 (respirable fraction)
Epoxy Resins and Hardeners
Risk: Skin sensitisation (permanent), asthma, eye and respiratory irritation
Controls: Nitrile gloves, RPE for spraying/heating, skin surveillance, avoid skin contact completely
Mineral Oils (neat cutting oils)
Risk: Dermatitis, scrotal cancer with prolonged skin contact, folliculitis
Controls: Skin contact minimisation, gloves, regular monitoring of oil condition, pre-employment and annual health check
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 16
Notes: Welding fume reclassification by IARC as a Group 1 carcinogen (same category as asbestos) in 2019 was a major regulatory event. HSE updated EH40 and issued updated guidance requiring LEV for all welding fume, indoor and outdoor. Many companies are still non-compliant.

## Slide 17
Your Responsibilities
What COSHH Requires From You
COSHH places legal duties not just on employers but on employees. You cannot opt out of these responsibilities. Failure to comply with COSHH requirements puts your health and the health of your colleagues at risk, and may result in disciplinary action.
1
Read and follow the COSHH assessment for every substance you use before you start work
2
Use all engineering controls provided (LEV, enclosed systems, ventilation) in the way they are designed to be used
3
Wear all PPE specified in the COSHH assessment correctly and for the full duration of the task
4
Attend health surveillance appointments arranged by your employer — failure to attend is a breach of your legal duty
5
Report any symptoms of skin irritation, respiratory difficulty, or ill health that may be work-related to your supervisor immediately
6
Report any defects in controls (LEV not working, PPE damaged, substances incorrectly stored or labelled) without delay
7
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 17
Notes: Section 7 of the Health and Safety at Work Act 1974 places the duty on employees to cooperate with health and safety measures. COSHH Regulation 14 specifically requires employees to use controls and attend health surveillance. These are legal duties, not requests.

## Slide 18
Nuclear Supply Chain
COSHH in the Nuclear Supply Chain
As part of the nuclear supply chain, your approach to hazardous substance management is under close scrutiny. Nuclear clients and the F4N assessment specifically examine your COSHH systems, records, and culture. A company that cannot demonstrate effective COSHH management will not win nuclear contracts.
Conservative approach to exposure
In nuclear culture, the principle of erring on the side of caution applies to COSHH just as it does to safety. Where there is uncertainty about whether a control is adequate, assume it is not and improve it. Do not assume 'it has always been done this way' means it is safe.
Documentation and traceability
Nuclear clients will ask to see COSHH assessment records, LEV test records, health surveillance records, and training records. These must be current, accessible, and clearly linked to specific substances and tasks. Records missing or out of date will be flagged.
Personal responsibility
Every individual in the nuclear supply chain is expected to take personal ownership of health and safety. If you see a COSHH control not being followed, you are expected to challenge it. This is a core nuclear safety culture behaviour.
Alignment with ISO 45001
COSHH management is a central element of an ISO 45001 occupational health and safety management system. F4N assessors will look for evidence that COSHH assessments are systematically reviewed, that exposure is monitored, and that health surveillance is completed and recorded.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 18
Notes: F4N verification assessors will look at the QHSE section and ask specifically about COSHH. They will want to see: the COSHH register, at least one worked COSHH assessment, LEV examination records, health surveillance records, and training records for this topic.

## Slide 19
Summary
Key Messages: What to Take Away
01
COSHH applies to all hazardous substances in your workplace. If it has an SDS, it is hazardous.
02
Chronic diseases develop silently over years. The damage can be permanent before symptoms appear.
03
Read your COSHH assessment and SDS before using any hazardous substance. Know the controls.
04
Engineering controls come before PPE in the hierarchy. LEV must be used correctly every time.
05
PPE must be the correct type and specification. Generic gloves or masks do not provide adequate protection.
06
Attend all health surveillance. Participate actively. Your results are your health record.
07
Report symptoms early. Skin irritation, breathing problems, or eye issues during work must be reported the same day.
08
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 19
Notes: Ask participants to commit to one action they will take in their area as a result of this training. Record actions. Follow up at the next team meeting or QHSE review.

## Slide 20
Next Steps
1
Locate and read the COSHH assessment for every substance you use in your area
2
Check you know where the Safety Data Sheets are kept at the point of use
3
Confirm your PPE is the correct specification for the substances you handle
4
Book your next health surveillance appointment if it is overdue
5
Report any COSHH concerns or symptoms to your supervisor today
Further Resources
COSHH Regulations 2002 (as amended)
HSG97 — A Step-by-Step Guide to COSHH Assessment
EH40 — Workplace Exposure Limits
HSE COSHH Essentials Tool — www.hse.gov.uk/coshh
Thank You
COSHH Awareness for Employees
Questions? Speak to your supervisor, QHSE lead,
or your NucCol Supply Chain Consultant.
Nuclear Collaboration Ltd
www.nuccol.co.uk
enquiries@nuccol.co.uk
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 20
Notes: Close by collecting attendance records. Issue action to complete a COSHH awareness confirmation form within one week. Follow up at next team briefing.