## Slide 1
QHSE Training Guide
Manual Handling:
Protecting Your
Body for Life
Understanding the risks, the law, and how to handle safely every day.
Aligned to: Manual Handling Operations Regulations 1992 | ISO 45001 | HSG115
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
The Law
Your Legal Duties: Manual Handling
The Manual Handling Operations Regulations 1992 (as amended 2002) require employers to, so far as is reasonably practicable: avoid hazardous manual handling operations; assess the risk where they cannot be avoided; and reduce the risk of injury to the lowest reasonably practicable level. Employees must follow safe systems of work and report issues.
1
Avoid
Can the task be mechanised, automated, or reorganised so that hazardous manual handling is not required? This is the preferred option and must always be considered first.
2
Assess
If manual handling cannot be avoided, a suitable assessment must be carried out using the TILE framework: Task, Individual, Load, Environment. See the next slides.
3
Reduce
Put controls in place to reduce the risk to the lowest reasonably practicable level. Use mechanical aids, change the task, improve the environment, provide training.
4
Employee duty
Employees must make use of any equipment provided, follow safe systems of work, and tell their employer if they become aware of a hazard or condition affecting their ability to handle safely.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
Risk Assessment
The TILE Framework: Assessing Manual Handling Risk
Before any manual handling task, the four factors of TILE must be considered. All four interact: a load that is manageable in ideal conditions may become hazardous when the environment, individual capability, or task demands change.
T
TASK
Does it involve twisting, stooping, or reaching?
Does it involve long carry distances or pushing/pulling?
Is it repetitive? Does it require sudden movements?
Is there sufficient rest between handling operations?
I
INDIVIDUAL
Does the person have any known health conditions?
Are they pregnant, recently returned from injury, or new to the job?
Do they have the right training and experience for this task?
Are they physically capable of the task in its current form?
L
LOAD
Is it heavy, bulky, unwieldy, or difficult to grip?
Does it have sharp edges, hot surfaces, or unstable contents?
Is the weight distribution uneven or unpredictable?
Could the load shift or move during handling?
E
ENVIRONMENT
Are floors even, clean, and free from obstructions?
Is there enough space to handle the load safely?
Is lighting adequate? Are there steps, ramps, or changes in level?
Is the temperature extreme? Are there strong air movements?
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3

## Slide 4
Safe Technique
The Safe Lifting Sequence: Step by Step
There is no single 'correct' way to lift that applies to every situation. What matters is planning the lift, keeping the spine in a neutral position, using the legs, and keeping the load close to the body. Follow these steps for lifting from a low level.
1
Plan before you lift
Check the weight, the destination, and the route. Clear the path. Can you use a mechanical aid? Do you need a second person? Decide before you touch the load.
2
Position your feet
Stand close to the load with feet shoulder-width apart. One foot slightly ahead of the other for balance. Face the direction of travel where possible.
3
Bend your knees
Squat down by bending the knees and hips. Keep your back in its natural curve — do not hunch it or hyper-extend it. Tuck your chin in slightly.
4
Get a firm grip
Grip the load securely. Use the full palm, not just the fingers. If the load is too heavy or awkward to grip safely, stop and get help or a mechanical aid.
5
Lift smoothly
Straighten the knees in a smooth, controlled movement. Do not jerk or twist as you lift. Keep the load close to your body throughout the movement.
6
Move and set down
Take small, controlled steps. Keep the load below chest height. To set the load down, reverse the process: bend the knees, keep the back straight, lower smoothly.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4

## Slide 5
Guidelines & Aids
Weight Guidelines and When to Use Mechanical Aids
The HSE publishes suggested weight guidelines as a starting point — not absolute limits. These assume ideal conditions: good posture, infrequent lifting, no twisting. Real conditions will often require lower limits. Where mechanical aids are available, they must be used.
25 kg
Men at knuckle height
Ideal, infrequent
16 kg
Women at knuckle height
Ideal, infrequent
-10%
Reduce for twisting
Per 45° of rotation
-30%
Reduce for frequency
Repetitive tasks
Mechanical Aids: Always Use Them When Available
Pallet truck / pump truck:
Moving loaded pallets across flat surfaces
Overhead hoist / crane:
Lifting and positioning heavy or awkward loads
Vacuum lifter:
Handling sheet materials, glass, and smooth-surfaced loads
Roller conveyor:
Moving boxes and totes along a fixed route
Height-adjustable workstation:
Eliminating the need to bend to floor level for operations
Team lift protocol:
Two or more persons with a designated lead for co-ordination
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 5
Notes: Stress that weight guidelines are NOT legal limits. They are risk indicators. Any manual handling that causes pain or injury is unacceptable regardless of the weight.

## Slide 6
Injuries & Reporting
Common Injuries and Why Reporting Matters
Musculoskeletal disorders (MSDs) from manual handling rarely result from a single incident. They accumulate over time. Early symptoms are warnings. Ignoring them allows permanent damage to develop. Report every sign of discomfort — not just injuries.
Common Manual Handling Injuries
Lower back pain and disc injuries — the most frequently reported MSD
Shoulder and rotator cuff strains from overhead or reaching movements
Wrist and forearm injuries from repetitive carry and grip tasks
Knee injuries from repeated deep squatting or kneeling on hard surfaces
Hernias from lifting loads that are too heavy, particularly with incorrect technique
Cumulative upper limb disorders (ULDs) from repetitive low-weight tasks
Report These Symptoms Immediately
Any pain, aching, or burning in the back, shoulders, arms, or legs after a handling task
Tingling or numbness in the hands or fingers during or after work
Stiffness that is worse in the morning and eases during the day
Swelling around a joint, particularly wrists, elbows, or shoulders
Pain that persists at weekends or during rest away from work
Any task that consistently causes discomfort — even if it feels manageable
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 6

## Slide 7
Safe Practice
Safe Manual Handling: Do and Do Not
Always Do These
Plan every lift before touching the load
Use mechanical aids whenever available — they exist for a reason
Keep the load as close to your body as possible throughout the carry
Bend your knees and keep your spine in a natural position when lifting from low level
Ask for help or use a team lift if the load is awkward, heavy, or unstable
Take regular breaks from repetitive handling operations
Report any pain, discomfort, or musculoskeletal symptom promptly
Never Do These
Do not twist your spine while carrying a load — turn with your feet
Do not rush a lift. A moment of carelessness can cause months of pain
Do not carry a load that obscures your line of sight
Do not ignore the discomfort, thinking it will go away
Do not attempt an unsafe lift because you think asking for help shows weakness
Do not carry loads that exceed your own safe limit without mechanical assistance
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 7

## Slide 8
Summary
Key Messages
01
Manual handling injuries build up over time. Do not wait for a serious incident before taking action.
02
TILE: always assess Task, Individual, Load, and Environment before handling.
03
Weight guidelines are not limits — they are starting points for assessment.
04
Bend the knees, keep the load close, do not twist. These three principles prevent the majority of back injuries.
05
Use mechanical aids. They are provided to protect you. Using them is not a sign of weakness.
06
Report symptoms early. Early treatment almost always prevents permanent damage.
07
You are legally required to follow safe systems of work and use the equipment provided.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 8

## Slide 9
Next Steps
1
Complete the TILE assessment for your most demanding manual handling task
2
Identify any mechanical aids available that are not currently being used
3
Report any recurring pain or discomfort to your supervisor today
4
Check your work area for manual handling hazards — poor floor surfaces, restricted space
Further Resources
Manual Handling Operations Regulations 1992
HSG115 — Manual Handling Guidance
HSE MAC Tool — Manual Handling Assessment Charts
ISO 45001:2018 — Occupational H&S Management
Thank You
Manual Handling: Protecting Your Body for Life
Questions? Speak to your supervisor, QHSE lead, or your NucCol Supply Chain Consultant.
Nuclear Collaboration Ltd
www.nuccol.co.uk
enquiries@nuccol.co.uk
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 9