## Slide 1
QHSE Training Guide
Fire Safety and
Emergency
Procedures
Understanding fire prevention, evacuation, extinguishers, and your responsibilities.
Aligned to: Regulatory Reform (Fire Safety) Order 2005 | ISO 45001 | BS 9999
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
The Law
Fire Safety Law: What It Requires
The Regulatory Reform (Fire Safety) Order 2005 (RRO) is the primary legislation governing fire safety in UK workplaces. It places duties on the 'Responsible Person' — typically the employer or building owner — and on all employees. Fire safety is everyone's responsibility.
Employer / Responsible Person
Carry out a fire risk assessment and keep it under review
Implement and maintain appropriate fire precautions
Provide fire safety information and training to all employees
Ensure fire detection, warning, and suppression systems are maintained
Establish and rehearse emergency evacuation procedures
Every Employee
Take reasonable care for their own fire safety and that of others
Cooperate with the employer's fire safety procedures
Use fire safety equipment only for its intended purpose
Report any fire hazards, defects in equipment, or concerns immediately
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
Fire Prevention
The Fire Triangle and Common Workplace Causes
Fire requires three elements to start and continue: fuel, heat, and oxygen. Remove any one of these and the fire cannot exist. Every fire prevention measure works by targeting one or more of these three elements.
FUEL
Combustible materials: wood, paper, cardboard, oils, plastics, solvents, gases
HEAT
Ignition sources: electrical faults, hot work, hot surfaces, static electricity, friction
OXYGEN
Typically air at 21% O2. Enclosed spaces may concentrate; some processes use enriched O2
Remove any one
to extinguish
Most Common Causes of Workplace Fires
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3

## Slide 4
Your Workplace
Know Your Building: What You Must Be Able to Locate
In a fire emergency, you will not have time to search for information. You must already know it. Every person on site must be able to locate these items and perform these actions without hesitation.
Fire alarm call points
Know the location of every manual call point on your route to the exit. You should be able to reach one within 30 seconds of detecting a fire.
Fire extinguishers
Know the type and colour coding of extinguishers in your area. Know which classes of fire each type is designed for. See the next slide.
Fire exits and routes
Walk your primary and secondary evacuation routes. Confirm they are unobstructed. Know which doors are fire doors and must remain closed.
Assembly point
Know the exact location of your designated assembly point. Know your alternative if the primary route is blocked. Never re-enter until authorised.
Emergency contacts
Know the number for emergency services (999), your site's fire safety officer or premises manager, and your nearest first aider.
Fire action notices
Posted throughout the building. Read them before an emergency — not during. Confirm they are up to date and clearly visible in your area.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4

## Slide 5
Extinguishers
Fire Extinguisher Types: Match the Extinguisher to the Fire
Using the wrong type of extinguisher on a fire can make it significantly worse. Never use water on an electrical or flammable liquid fire. Know the types in your area before you need them.
Water (Red)
Use for: Paper, wood, textiles (Class A)
Avoid: Electrical fires. Flammable liquids.
CO2 (Black)
Use for: Electrical equipment. Flammable liquids (Class B/E)
Avoid: Do not use in confined spaces. No knock-back effect.
Dry Powder (Blue)
Use for: Flammable liquids, gases, electrical (B/C/E)
Avoid: Damages equipment. Poor visibility when discharged.
Foam (Cream)
Use for: Flammable liquids (Class B). Also Class A
Avoid: Do not use on electrical fires or cooking oils.
Wet Chemical (Yellow)
Avoid: Not suitable for Class B or electrical fires.
P.A.S.S technique: Pull the pin | Aim at the base of the fire | Squeeze the handle | Sweep side to side. Only tackle a fire in its earliest stages and when you have a clear exit behind you.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 5

## Slide 6
Prevention
Fire Doors and Hot Work: Two Critical Controls
Two of the most common fire safety failures in manufacturing workplaces are propped-open fire doors and hot work carried out without proper controls. Both are easily preventable and both have caused fatalities.
Fire Doors: Never Prop Them Open
A closed fire door can hold back fire and smoke for 30-60 minutes — it is a physical life safety device
A propped-open fire door removes this protection entirely and may render the building's fire strategy ineffective
Fire doors must be self-closing. Report any door with a damaged or missing self-closer immediately
Never wedge, prop, or deliberately hold open a fire door, even temporarily
Regularly check that fire doors in your area close fully and latch correctly. Report any defects
Hot Work Permit: Always Required
All welding, cutting, grinding, and brazing must be covered by a signed hot work permit before work starts
Clear the area within 3 metres of all combustible materials before work begins
Have a fire extinguisher of the correct type immediately to hand throughout the operation
Assign a dedicated fire watcher to monitor during the work
Carry out a 30-minute fire watch after hot work ends — fires can smoulder for up to an hour undetected
Return and re-inspect the area 1 hour after the fire watch ends
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 6

## Slide 7
Evacuation
What to Do When the Fire Alarm Sounds
There is one rule when the fire alarm sounds: leave. Do not investigate. Do not collect belongings. Do not wait to see if the alarm is a false alarm. Every second of delay reduces the margin of safety. The following steps must be followed in order.
1
Stop what you are doing
Switch off any equipment that poses an immediate risk if left unattended, if this can be done in under 5 seconds. Do not stop for anything else.
2
Leave by the nearest safe exit
Use the primary exit if clear. If not, use your secondary route. Do not use lifts. Do not run but walk purposefully and calmly.
3
Close doors behind you
Close all doors as you leave — do not lock them. Closed doors slow the spread of fire and smoke and can save lives.
4
Proceed to the assembly point
Go directly to your designated assembly point. Do not divert to your car, collect colleagues from other areas, or re-enter the building for any reason.
5
Report to your fire warden
Confirm your presence at the assembly point. Fire wardens must account for every person. Do not leave the assembly point without permission from a fire warden.
6
Do not re-enter
Do not re-enter the building until the Responsible Person, fire warden, or fire service confirms it is safe to do so. This authority cannot be delegated to a colleague.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 7

## Slide 8
Summary
Key Messages
01
Fire requires fuel, heat, and oxygen. Remove any one and the fire cannot continue.
02
Know your evacuation route, your assembly point, and the alarm signal for your area before a fire — not during it.
03
Never use the wrong type of extinguisher. Know the types in your area. Use P.A.S.S.
04
Fire doors must never be propped open. A closed fire door can hold back fire for up to 60 minutes.
05
Hot work permits are mandatory for all welding, grinding, and cutting. The 30-minute fire watch is not optional.
06
When the alarm sounds — leave immediately. Do not collect belongings. Do not investigate. Do not re-enter.
07
Report fire hazards, damaged equipment, or obstructed exits as soon as you find them.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 8

## Slide 9
Next Steps
1
Walk your evacuation route and confirm your assembly point today
2
Check fire extinguisher types in your area — do you know what each one is for?
3
Confirm there are no obstructions in fire exits or on evacuation routes
4
Report any fire door defects, damaged detection equipment, or hazards to your supervisor
Further Resources
Regulatory Reform (Fire Safety) Order 2005
BS 9999 — Fire Safety in Design, Management and Use of Buildings
HSE Fire Safety Guidance
ISO 45001:2018 — Occupational H&S Management
Thank You
Fire Safety and Emergency Procedures
Questions? Speak to your supervisor, QHSE lead, or your NucCol Supply Chain Consultant.
Nuclear Collaboration Ltd
www.nuccol.co.uk
enquiries@nuccol.co.uk
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 9