## Slide 1
QHSE Training Guide
Working at Height:
Preventing Falls
Understanding the regulations, hierarchy of controls, and safe equipment selection.
Aligned to: Work at Height Regulations 2005 | ISO 45001 | BS 8454
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
The Law
Work at Height Regulations 2005: What They Require
The Work at Height Regulations 2005 apply wherever there is a risk of a fall liable to cause personal injury. This is not limited to rooftops or scaffolding. It includes stepladders, mezzanine floors, loading bays, pits, and any position from which a person could fall and be injured.
The Three Core Requirements
1. AVOID — Do not work at height if it is reasonably practicable to carry out the work safely from the ground
2. PREVENT — If working at height is necessary, prevent any person falling using collective measures such as guardrails and platforms first
3. MITIGATE — If the risk of falling cannot be eliminated, minimise the consequences using fall arrest systems, safety nets, or other mitigating measures
Employer duty
Plan, organise, and carry out all work at height safely. Ensure work is only done by competent people. Ensure equipment is suitable, inspected, and properly maintained.
Employee duty
Use any equipment or safety devices provided correctly. Report any safety concerns, defects, or incidents immediately. Do not work at height unless trained and authorised.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
Control Hierarchy
Selecting the Right Equipment: The Hierarchy
The Regulations specify a hierarchy for work at height. You must work down this hierarchy — using the safest option that is practicable for the task. You cannot go straight to a ladder simply because it is convenient.
1. Collective prevention | Most Effective
Scaffold, work platform, MEWP with edge protection. The working area is made safe for everyone. No individual action required.
2. Collective fall arrest
Safety nets, airbags, or other systems that catch a person if they fall. Reduces severity of fall but does not prevent it.
3. Personal fall restraint
Personal fall restraint (harness and lanyard) that prevents the wearer reaching the fall hazard. Must be anchored correctly.
4. Personal fall arrest
Arrest system (self-retracting lifeline, energy-absorbing lanyard) that stops a fall that has occurred. Requires rescue plan.
5. Ladders and stepladders | Least Effective
Only acceptable for low-risk, short-duration work where other equipment is not reasonably practicable. Subject to strict conditions.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3

## Slide 4
Ladders
Ladder Safety: The Conditions That Make It Acceptable
Ladders and stepladders are only acceptable under the Regulations where other equipment is not reasonably practicable AND the risk assessment confirms the task is of short duration and low risk. Using a ladder must be a considered decision, not the default.
When Using a Ladder: Must-Do
Inspect the ladder before every use — check rungs, stiles, feet, and locking mechanisms
Set the ladder at the correct angle: 1 unit out for every 4 units up (75 degrees)
Secure at the top against a firm surface, or have a competent person foot the ladder
Maintain three points of contact at all times — two feet and one hand, or two hands and one foot
Keep your body centred between the stiles. Do not overreach — move the ladder
Ensure adequate footwear — no smooth-soled shoes, nothing wet or muddy
When Using a Ladder: Never Do
Never use a damaged or defective ladder. Remove from service, label, and report immediately
Never lean a ladder against fragile, unstable, or unsecured surfaces
Never use a stepladder for sustained work. If the task takes more than 30 minutes, use a platform
Never carry loads that prevent maintaining three points of contact
Never work from the top two rungs of a ladder or the top three steps of a stepladder
Never allow a ladder to project less than 1 metre above the landing point unless an alternative handhold exists
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4

## Slide 5
Equipment
Scaffolding, MEWPs, and Edge Protection: Key Rules
Collective prevention measures — scaffolding, mobile elevated work platforms (MEWPs), and fixed edge protection — provide the highest level of protection for working at height. Each has specific requirements that must be met.
Scaffold
Must be designed, erected, altered, and dismantled by trained and competent persons (CISRS card for TG20 compliance in the UK)
Must be inspected by a competent person before use, after any event likely to affect stability, and at least every 7 days
Inspection record must be completed and retained. Tag system must show current inspection status
Never overload scaffold boards with plant, equipment, or materials beyond the design load
Mobile Elevated Work Platforms (MEWPs)
Operators must hold a recognised MEWP operator certificate (IPAF or equivalent) for the class of machine
Conduct a pre-use check before every operation. Complete the manufacturer's daily check record
Always wear and anchor a harness in scissor lifts (working platform) and boom lifts (harness mandatory)
Never outreach beyond the platform edge. Never use MEWPs in conditions that exceed wind speed limits
Edge Protection (fixed)
Guardrail systems at height must include: top rail at 950-1150mm, intermediate rail, and toeboard
Toe boards must be at least 150mm high to prevent objects being kicked off the edge
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 5

## Slide 6
Additional Hazards
Dropped Objects, Weather, and Exclusion Zones
Working at height creates hazards not just for the person working, but for anyone below. Dropped objects, deteriorating weather, and uncontrolled access to the area below are all significant risks that must be managed as part of the risk assessment.
Dropped Objects
Tools, fixings, and materials must be secured or tethered where practicable
Use tool lanyards for any hand tool being used at height
Do not place unsecured items on scaffold boards or platforms
Debris netting or fan protection must be in place over public or occupied areas below
Exclusion zone must be established before work begins and maintained throughout
Weather and Environment
Do not work at height in strong winds — check manufacturer limits for MEWPs and scaffolds
Wet surfaces dramatically increase slip risk on ladders, boards, and platforms
Ice and frost on access equipment must be cleared before use
Low light and poor visibility increase risk. Ensure adequate lighting for all height work
Heat stress and dehydration increase fatigue and risk of misjudgement at height
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 6

## Slide 7
Summary
Key Messages
01
Any position from which a fall could cause injury is 'at height' under the Regulations.
02
Avoid, prevent, mitigate. Follow the hierarchy. Never go straight to a ladder without considering alternatives.
03
Ladders are for short-duration, low-risk tasks only. They are at the bottom of the hierarchy, not the starting point.
04
Inspect all access equipment before every use. Defective equipment must be removed from service immediately.
05
Always establish an exclusion zone below height work before starting.
06
Personal fall arrest requires a rescue plan. Suspension trauma can develop within minutes.
07
Do not work at height alone unless a specific risk assessment confirms this is safe and a system is in place.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 7

## Slide 8
Next Steps
1
Review the risk assessment for every working at height task in your area
2
Check the inspection records for all access equipment — are they current?
3
Walk the area below any height work to identify exclusion zone requirements
4
Confirm all height workers are trained and authorised for their equipment
Further Resources
Work at Height Regulations 2005
HSG150 — Health and Safety in Construction
IPAF — International Powered Access Federation
HSE Ladder Exchange Campaign — www.hse.gov.uk
Thank You
Working at Height: Preventing Falls
Questions? Speak to your supervisor, QHSE lead, or your NucCol Supply Chain Consultant.
Nuclear Collaboration Ltd
www.nuccol.co.uk
enquiries@nuccol.co.uk
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 8