## Slide 1
QHSE Training Guide
Electrical Safety
Awareness
Understanding electrical hazards, inspection, isolation, and what to do in an emergency.
Aligned to: Electricity at Work Regulations 1989 | IET Wiring Regulations (BS 7671) | ISO 45001
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
The Hazard
Why Electricity Is Uniquely Dangerous
Electricity cannot be seen, heard, or smelled. Unlike most physical hazards, the warning signs are often invisible until contact has already occurred. In a manufacturing environment, every electrical system, portable tool, and extension lead carries risk. Understanding that risk is the first step to managing it.
Electric shock
Current passing through the body causes muscle contraction, cardiac arrest, and respiratory failure. As little as 50 milliamps (0.05A) can cause ventricular fibrillation. Mains voltage (230V AC) is potentially fatal.
Electrical fire
Overloaded circuits, damaged insulation, and loose connections generate heat that ignites surrounding materials. Electrical fires account for around 20% of all accidental fires in non-domestic premises.
Arc flash and explosion
Short circuits can release enormous energy in fractions of a second, producing temperatures exceeding 20,000°C, pressure waves, and molten metal projectiles. Arc flash can cause severe burns at distances of several metres.
Indirect causes
Electric shock often causes secondary injuries: falls from height, involuntary muscle movements causing impact injuries, or fires started by the fault. The secondary injury can be as serious as the shock itself.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2
Notes: 50mA = 0.05A. A standard torch battery is 1500mA. Mains voltage drives 230/R amps through the body. At typical skin resistance of 1000 ohms, that is 230mA — over 4 times the lethal dose. Voltage is not the killer; current is. But voltage drives the current.

## Slide 3
The Law
Electrical Safety: The Legal Framework
Multiple pieces of legislation govern electrical safety in UK workplaces. The Electricity at Work Regulations 1989 are the primary specific standard, but the Health and Safety at Work Act 1974, PUWER 1998, and the IET Wiring Regulations all apply.
Electricity at Work Regulations 1989
1. All electrical systems must be constructed to prevent danger, so far as reasonably practicable 2. Electrical equipment must be maintained to prevent danger 3. No person shall work on or near a live conductor unless it is not reasonably practicable to make it dead, AND it is reasonable in all circumstances, AND suitable precautions are taken to prevent injury 4. Only competent persons may carry out electrical work
PUWER 1998 — Portable Electrical Equipment
1. Portable electrical equipment used at work must be suitable for its intended use 2. It must be maintained in a safe condition — this includes visual inspection and where appropriate, formal in-service inspection and testing (commonly known as PAT testing) 3. Records of inspection and testing must be kept
IET Wiring Regulations (BS 7671) — 18th Edition
1. The national standard for the design, erection, and verification of electrical installations in the UK 2. Compliance with BS 7671 provides presumption of compliance with the Electricity at Work Regulations 3. Periodic inspection and testing of fixed installations required at intervals based on installation type and use
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3

## Slide 4
Equipment Inspection
Pre-Use Inspection: What to Check Before Every Use
Visual inspection before every use is your most important electrical safety check. Most portable electrical faults are visible before they cause harm. The 30-second inspection you carry out before plugging in a tool could prevent a fatality.
Cable
Insulation intact — no cuts, abrasion, burn marks, or crushing
No kinking, excessive bending, or stretching close to plug or appliance
No joins, tape repairs, or improvised connections
Conductors not visible through the outer sheath
Plug
Casing intact — no cracks, damage, or missing parts
Cover screws present and tight — cable grip functioning
Cable not entering plug at an angle (suggests cable stress)
Pins undamaged, not bent, discoloured, or corroded
Appliance body
Casing intact — no cracks, missing covers, or exposed internal parts
Ventilation slots clear and unobstructed
No signs of overheating: discolouration, burn marks, or melted insulation
Labels and rating plates legible and consistent with the use environment
Labelling
In-service inspection label present and within date
PAT test label or record showing last test date (where formally required)
Voltage and wattage rating appropriate for the supply it is being used with
No label indicating 'Do Not Use' or 'Quarantined' — never override these tags
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4

## Slide 5
Isolation: LOTO
Lockout/Tagout: The Mandatory Isolation Procedure
Lockout/Tagout (LOTO) is a safety procedure that ensures hazardous energy sources — electrical, mechanical, hydraulic — are isolated and cannot be re-energised while maintenance, repair, or cleaning work is being carried out. It is a legal requirement where applicable.
1
Notify
Inform all affected personnel that the equipment is being isolated. Agree who is responsible for the isolation. Check no one is working on or near the equipment.
2
Identify
Identify ALL energy sources for the equipment — electrical isolators, pneumatic valves, hydraulic shut-offs, stored spring energy. Mark each one.
3
Isolate
Switch off the equipment using its normal stop controls. Then open and isolate each energy source — turn off at the isolator, not just at the machine's own switch.
4
Lock
Apply a padlock to each isolation point. Each person working on the equipment applies their own lock. The equipment cannot be re-energised until ALL locks are removed.
5
Tag
Attach a danger tag to each isolation point and the machine. The tag identifies who locked out, the date and time, and the reason. Do not remove another person's lock.
6
Try
Attempt to start the equipment using its normal controls. Confirm it does not start. Test for live voltage using an approved voltage indicator before touching conductors.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 5
Notes: LOTO is non-negotiable. More workers are killed each year by inadvertent re-energisation during maintenance than by any other electrical cause. 'I thought it was off' or 'someone else must have switched it back on' are the most common pre-incident findings.

## Slide 6
Practical Safety
RCDs, Safe Voltages, and Extension Lead Safety
Three practical measures that significantly reduce electrical risk in manufacturing environments: using residual current devices, reducing operating voltage for portable tools, and managing extension leads and temporary supplies correctly.
Residual Current Devices (RCDs)
1. An RCD detects small differences in current that indicate a fault, such as current leaking through a person, and disconnects the supply in 30-40 milliseconds — fast enough to prevent cardiac arrest | 2. All portable electrical equipment used outdoors or in damp environments must be protected by an RCD | 3. RCDs must be tested by pressing the test button before use. They can fail silently without this test | 4. RCDs do not protect against direct contact with live conductors between line and neutral. They are not a substitute for isolation.
Reduced Low Voltage (110V CTE)
1. 110V centre-tapped-to-earth (CTE) supply is standard practice for portable tools on construction sites and is increasingly used in manufacturing | 2. At 110V CTE, the maximum voltage to earth is 55V — significantly less likely to cause cardiac arrest than 230V | 3. Tool transformers must be inspected and maintained. They do not eliminate risk — they reduce it | 4. Where 110V is available, it must be used in preference to 230V for portable power tools
Extension Leads and Temporary Supplies
1. Extension leads are temporary supplies. They must not form part of a permanent installation | 2. Reels must be fully unwound during use to prevent overheating. Coiled cables under load get hot | 3. Never join extension leads with adaptors to achieve greater length. Use a single lead of the required length | 4. Do not route extension leads under carpets, through doorways where they will be crushed, or across walkways without protection
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 6

## Slide 7
Emergency Response
Responding to an Electric Shock Incident
An electric shock incident requires an immediate, controlled response. The first priority is always to isolate the electrical supply before touching the casualty. Touching a person in contact with live electrical supply will electrocute the rescuer.
1
Do NOT touch
Do not touch the casualty until you are certain they are no longer in contact with a live electrical source. You will receive a shock if you do.
2
Isolate the supply
Switch off the power at the nearest isolator, fuse board, or supply point. If you cannot reach the isolator safely, use a non-conductive object (dry wood) to push the person clear.
3
Call for help
Call 999 immediately if the person is unconscious, not breathing, or has significant burns. Alert your first aider and supervisor at the same time.
4
First aid / CPR
Once isolated, begin first aid. If not breathing, start CPR. Electric shock can cause cardiac arrest that responds well to early CPR and defibrillation.
5
Do not leave
Stay with the casualty and reassure them. Even if they appear uninjured, all electric shock victims must be assessed by a medical professional — cardiac complications can develop hours later.
6
Preserve the scene
Do not touch or disturb the equipment or supply system. The scene must be preserved for investigation by the relevant authorities (HSE, police) under RIDDOR.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 7

## Slide 8
Summary
Key Messages
01
Electricity cannot be seen or heard. Invisible faults can kill. Inspect your equipment before every use.
02
You must never carry out electrical work unless you are a qualified and authorised electrician.
03
LOTO must be applied before any maintenance, repair, or cleaning of electrically powered equipment.
04
Test with an approved voltage indicator before touching any electrical component — even after isolation.
05
RCDs must be tested before every use. A failed RCD may give no warning sign.
06
In an electric shock emergency: isolate first, then approach the casualty. Do not touch a live casualty.
07
All electric shock incidents requiring medical treatment must be reported under RIDDOR.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 8

## Slide 9
Next Steps
1
Inspect all portable electrical equipment in your area before your next shift
2
Confirm the location of isolation points for every machine you operate
3
Test the RCD on your portable supply before your next use
4
Report any damaged cables, defective equipment, or electrical concerns today
Further Resources
Electricity at Work Regulations 1989
HSE HSG107 — Maintaining Portable and Transportable Electrical Equipment
IET Wiring Regulations BS 7671 — 18th Edition
ISO 45001:2018 — Occupational H&S Management
Thank You
Electrical Safety Awareness
Questions? Speak to your supervisor, QHSE lead, or your NucCol Supply Chain Consultant.
Nuclear Collaboration Ltd
www.nuccol.co.uk
enquiries@nuccol.co.uk
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 9