## Slide 1
NUCLEAR HUMAN PERFORMANCE TOOLS
Seven tools every nuclear worker applies on every safety-significant task
HP-1
Pre-Job Briefing
Before every nuclear task: scope, procedure, error traps, hold points, stop-work criteria
HP-2
Self-Check (STAR)
Stop, Think, Act, Review: before every safety-significant action
HP-3
Peer Check
Independent second-person check before acting on Grade 1/2 work
HP-4
3-Way Communication
Sender states, receiver repeats back, sender confirms
HP-5
Place Keeping
Mark each step on procedure. Never rely on memory alone
HP-6
Concurrent Verification
Two people independently verify critical measurements simultaneously
HP-7
Stop-Work Authority
ANY person. ANY time. ANY concern. Cannot be overridden.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
NUCLEAR ERROR TRAPS: SPOT THEM BEFORE THEY GET YOU
When you spot an error trap: use more HP tools, not fewer
1. Time Pressure
Increase HP tool use
2. Distraction
Increase HP tool use
3. Habit / Complacency
Increase HP tool use
4. First Time / Infrequent
Increase HP tool use
5. Overconfidence
Increase HP tool use
6. Unclear Procedure
Increase HP tool use
7. Poor Environment
Increase HP tool use
8. Simultaneous Tasks
Increase HP tool use
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2