## Slide 1
TALK 1 OF 3
What is CFSI and Why Does It Matter?
Talk 1 of 3: Definitions, risks, and the nuclear supply chain obligation
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
What Does CFSI Mean?
CFSI stands for Counterfeit, Fraudulent, and Suspect Items
Counterfeit: items made or altered to look like a genuine product without authorisation
Fraudulent: items intentionally misrepresented through false documentation or identity
Suspect: items where something suggests they may not be genuine, pending investigation
CFSI includes documentation and certification, not just physical items
Every one of us in this organisation has a role in preventing CFSI from entering our nuclear work.
NSS-03j | TALK 1 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
Why CFSI Is a Critical Nuclear Risk
A CFSI component in a safety-critical application can fail without warning in service
CFSI corrupts the traceability that underpins the nuclear facility safety case
Nuclear regulations require CFSI incidents to be reported to the regulator via the licensee
Knowing introduction of CFSI into a nuclear application can result in criminal liability
The financial and reputational consequences for a company found responsible are severe
This is not a theoretical risk. CFSI incidents have been confirmed in the UK nuclear supply chain.
NSS-03j | TALK 1 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3

## Slide 4
The Scale of the Problem
Approximately 10% of all worldwide manufactured products are estimated to be counterfeit
Fasteners, mechanical components, and electronic components are among the most counterfeited items in industrial supply chains
ONR has issued multiple CFSI alert notices targeting specific product categories in the nuclear supply chain
Grey market supply, obsolete items becoming 'available', and below-market pricing are the most common entry routes
Certification documents are as likely to be fraudulent as the items themselves
The CFSI threat changes constantly. New incidents are added to the industry alert database regularly.
NSS-03j | TALK 1 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 4

## Slide 5
Your Obligation
Everyone in purchasing, goods receipt, stores, and production has a CFSI obligation
Purchasing staff: know the at-risk procurement scenarios and act on them
Goods receipt staff: apply the CFSI checklist to every nuclear contract delivery
Anyone: if something does not look right, report it immediately, do not pass it through
Quality Manager: notified the same day any concern is identified
No suspected CFSI item may be used, released, or returned without Quality Manager sign-off
The CFSI Goods Receipt Checklist (NSS-03h) and Suspect Item Report Form (NSS-03i) are the working tools for this.
NSS-03j | TALK 1 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 5

## Slide 6
Discussion Scenario
SCENARIO
A batch of fasteners arrives for use on a Grade 2 nuclear component. The price was 40% below your usual supplier's quote. The delivery came from a distributor you have not used before. The certificates look fine at first glance.
DISCUSS:
What warning signs are present here? What should happen before these fasteners are used on the nuclear component?
NSS-03j | TALK 1 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 6

## Slide 7
CFSI starts in the supply chain. It ends at the point where someone stops it. That person could be any of us.
NSS-03j | TALK 1 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 7

## Slide 8
TALK 2 OF 3
Warning Signs at Purchasing and Goods Receipt
Talk 2 of 3: The indicators to look for before and when items arrive
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 8

## Slide 9
Two Lines of Defence
CFSI prevention has two distinct stages: purchasing and goods receipt
Purchasing defence: recognise risk before you order, and apply enhanced scrutiny
Goods receipt defence: inspect every delivery on a nuclear contract against the nine warning sign categories
Both lines matter. Passing either without adequate checks creates a CFSI risk
The checklists and tools exist so neither defence relies on individual judgement alone
Refer to NSS-03g Section 3 for purchasing warnings and Section 4 for goods receipt warnings.
NSS-03j | TALK 2 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 9

## Slide 10
6 Purchasing Warning Signs
1
Unusual Availability
Obsolete or hard-to-source item suddenly available from a non-approved source
2
Unusual Supplier / Location
Item offered by a supplier or from a country you have not used before
3
Below-Market Price
Price significantly lower than market rate or your previous purchases
4
Short Lead Time
Delivery offered much faster than normal for this item type
5
Unverifiable Ownership Chain
Traceability to the OEM cannot be established
6
Grey Market Supply
Not supplied by the OEM or an OEM-authorised distributor
NSS-03j | TALK 2 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 10

## Slide 11
9 Goods Receipt Warning Signs (Part 1: Documentation and Physical)
1
Paperwork Anomalies
Poor spelling, grammar errors, signs of tampering, incorrect or missing information
2
Certificate Issues
Alterations, Tippex, not traceable to items, or superseded standards referenced
3
Packaging Differences
Colour, font, logo, or layout different from previous genuine deliveries
4
Product Condition
Evidence of rework, refinishing, or repainting on the items
5
ID Mark Anomalies
Marks altered, missing, smudged, or using a different marking method than expected
6
Lot Information Issues
Batch/serial numbers unusual for this supplier or missing entirely
NSS-03j | TALK 2 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 11

## Slide 12
9 Goods Receipt Warning Signs (Part 2: Certification and Appearance)
7
OEM Cert Missing
Manufacturer certification absent, untraceable, or using electronic signature when wet signature is required
8
Physical Appearance Differences
Colour, shape, size, weight, or finish does not match specification or previous deliveries
9
Quantity / Lot Anomaly
Delivered quantity does not match PO, or lot size inconsistent with known production volumes
NSS-03j | TALK 2 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 12

## Slide 13
Discussion Scenario
SCENARIO
A delivery arrives. The quantity is correct. The delivery note looks fine. But one person on the goods receipt team notices that the markings on the components look slightly different from the last batch, and the certificates have a typed signature where previous certificates had a wet ink signature.
DISCUSS:
Does this trigger a CFSI concern? What should happen next?
NSS-03j | TALK 2 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 13

## Slide 14
One person who notices something unusual and acts on it can stop CFSI entering a nuclear facility. Be that person.
NSS-03j | TALK 2 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 14

## Slide 15
TALK 3 OF 3
What to Do If You Suspect CFSI
Talk 3 of 3: The four-step response and reporting obligations
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 15

## Slide 16
The Four-Step Response
Step 1: STOP and QUARANTINE. Do not use, process, return to stores, or send back to the supplier
Step 2: REPORT to the Quality Manager immediately, the same working day
Step 3: DO NOT INVESTIGATE ALONE. The Quality Manager takes over. Do not call the supplier
Step 4: RETAIN ALL EVIDENCE. The item, packaging, documentation, and photos exactly as received
Complete the CFSI Suspect Item Report Form (NSS-03i) as part of Step 2. This is a controlled quality record.
NSS-03j | TALK 3 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 16

## Slide 17
What Quarantine Means
Physical quarantine: the item must be physically moved to a designated quarantine area
Labelling: the quarantine area and the item must be clearly labelled 'SUSPECT CFSI - DO NOT USE, PENDING INVESTIGATION'
No movement: the item must not leave quarantine without written Quality Manager authorisation
No return: do NOT return the item to the supplier without Quality Manager and potentially ONR involvement
All packaging, documentation, and photographs must remain with the item
An informal 'I'll keep an eye on it' is not quarantine. Physical isolation and clear labelling are required.
NSS-03j | TALK 3 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 17

## Slide 18
Reporting Up the Chain
Nuclear client notification: Grade 1 significance items must be notified to the client within 24 hours
The Quality Manager assesses significance and owns the client communication
ONR notification: where a confirmed CFSI has potential nuclear safety significance, the licensee is responsible for notifying ONR
Industry OPEX reporting: confirmed CFSI should be shared via SDF Supply Chain Quality Working Group and NIA channels
The Suspect Item Report Form (NSS-03i) records the full reporting trail as a lifetime quality record
Confirmed CFSI incidents shared across the industry have prevented the same item from being used on other nuclear sites.
NSS-03j | TALK 3 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 18

## Slide 19
What Not to Do
Do NOT use the item just because you are not certain it is CFSI. Uncertainty is the trigger for quarantine, not for release
Do NOT contact the supplier to resolve a CFSI concern yourself without Quality Manager involvement
Do NOT return the item to stores, the production area, or the supplier without authorisation
Do NOT assume someone else will deal with it. The person who identifies the concern is responsible for starting the process
Do NOT discard, repackage, or clean the item before investigation. Evidence must be preserved
None of these actions make the problem go away. They make it worse and expose the company to regulatory and legal risk.
NSS-03j | TALK 3 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 19

## Slide 20
Discussion Scenario
SCENARIO
You have just completed a CFSI goods receipt check and identified two warning signs on a batch of valves. Your supervisor says 'we have a delivery deadline tomorrow, can we just use them and raise a concern report afterwards?'
DISCUSS:
What does the four-step response tell you to do? Who do you need to involve and when?
NSS-03j | TALK 3 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 20

## Slide 21
If in doubt, stop. Report it. Protect the nuclear facility, protect the company, and protect yourself.
NSS-03j | TALK 3 OF 3
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 21