## Slide 1
NUCLEAR QUALITY STANDARDS
What they are, how they relate, and what they mean for you
NUCLEAR SITE LICENCE CONDITIONS
ONR licence requirements governing the site operator
ISO 19443
Nuclear supply chain QMS - additional requirements beyond ISO 9001 for ITNS work
ISO 9001
General quality management system - the foundation all nuclear suppliers must hold
SPECIFIC CODES: ASME NQA-1 | RCC-M | ISO 17025 | BS EN codes
Applied at component, project, or application level as specified by the client
GRADE 1
Direct nuclear safety impact
GRADE 2
Indirect nuclear safety impact
GRADE 3
Operating performance impact
GRADE 4
Commercial grade - no safety impact
Your nuclear client specifies the quality grade for your scope. If no grade is specified, ask before you start. Never assume a lower grade than required.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 1

## Slide 2
ISO 19443: WHAT IT DEMANDS OF YOU
The seven additional requirements that go beyond ISO 9001
CULTURE
Nuclear quality culture: visible leadership commitment to quality as a nuclear safety priority
ITNS
ITNS scope: formally determine and document which products and services are Important to Nuclear Safety
SQEP
SQEP: every person on safety-significant work must be demonstrably suitably qualified and experienced
RECORDS
Lifetime records: quality records for ITNS work retained for the life of the facility, typically 40+ years
NCR
Nuclear NCR: non-conformances graded for safety significance; concessions require formal approval
SUPPLY CHAIN
Supply chain: qualified suppliers, CFSI controls, nuclear requirement flow-down, right of access
TRACEABILITY
Traceability: full material and process traceability from finished item back to source material
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 2

## Slide 3
CFSI: WHAT TO WATCH FOR AND WHAT TO DO
Counterfeit, Fraudulent, and Suspect Items - everyone in this building has a role
KEY WARNING SIGNS
1
Price well below market rate
2
Item suddenly available from unusual source
3
Packaging or labelling looks different
4
Markings on items altered or missing
5
Certificate has Tippex, typed signatures, or untraceable lot numbers
6
Physical appearance differs from previous deliveries
IF YOU SPOT CFSI: 4 STEPS
1
STOP and QUARANTINE
Do not use, process, or return. Label clearly.
2
REPORT to Quality Manager
Same working day. Complete NSS-03i form.
3
DO NOT investigate alone
Quality Manager takes over. Do not call supplier.
4
RETAIN ALL EVIDENCE
Item, packaging, docs, photos as received.
NucCol | Nuclear Collaboration Ltd · Fit For Nuclear Programme · Commercial in Confidence | 3